## Slide 1: High Level Architecture (HLA)
Don McGregor
Don Brutzman
MOVES Institute
brutzman@nps.edu

## Slide 2: HLA History
DIS was the original standard for DoD M&S, but it was limited in some ways
  Designed for virtual worlds, and that’s all
  No concept of a simulation clock; all open loop
So HLA was designed by DMSO and MIT in the early/mid 90’s. It was intended to be the One True Standard for DoD M&S and to supplant DIS. It has not quite worked out that way.
1996: HLA is the standard for DoD M&S, all simulations must comply with HLA by 2001 or receive a waiver
Never Underestimate the Installed Base

## Slide 3: HLA
The original idea was to use HLA everywhere,
All services standardize on HLA
A tad bit ambitious given the technology and nature of M&S, funding, installed base, migration, diverse applications, diverse use cases, etc. etc.

## Slide 4: HLA
HLA has three major differences from DIS
  The API is standardized, rather than the format of messages
  The object-oriented model information (and some setup data) to be exchanged is configurable, thus matching any model
  It can optionally use a simulation clock (or perhaps uses a parallel DES clock with rollback)

## Slide 5: DIS versus HLA
What do you standardize in your standard?
DIS standardizes packet format on the wire, but not the API
DIS PDU
DIS API A
DIS API B3

## Slide 6: DIS versus HLA
You need an API to read/write DIS PDUs, but this API is not standardized
If you change DIS library vendors, you will have to change all code that touches the DIS API
DIS API for
Open-DIS
Simulator
Graphics API
Physics API

## Slide 7: HLA versus DIS
On the other hand, the packets are in a standard format, so any application that reads the format can be used, including multiple languages (C, C++, Java, Objective-C, C#, ADA, etc.)
Interesting tradeoffs, both from perspective of near-term “how do we do it” plus also long-term enterprise maintainability and evolution

## Slide 8: HLA vs DIS
HLA takes a different approach from DIS
HLA standardizes the API, while remaining silent on the packet format.
Opaque Packet Format
HLA API
HLA API

## Slide 9: HLA vs DIS
The benefit to this is that you can swap out HLA implementations without changing your source-code API. In fact, you can simply swap DLLs in Windows
HLA API
Simulator
Graphics API
Physics API
Replaceable HLA module

## Slide 10: DIS vs HLA
This allows vendors to innovate capabilities under the API. If someone comes up with a better Area of Interest scheme or a “better” (proprietary) way to reduce bandwidth use, they can do that within a common code API.
The drawback to this is that a simulation running a Pitch HLA implementation will not be able to talk to a simulation running a MaK HLA implementation, or other HLAs.

## Slide 11: DIS vs HLA
The wire format incompatibility can be mitigated via the use of gateways
In a multiplatform environment in can be a challenge to get all boxes on the same version of HLA from the same vendor
Sim runs on Windows, Linux; do they all have Pitch HLA-NG release x.x?
Runs HLA
From Both
Vendors

## Slide 12: Configurable Simulation Data
DIS PDUs have data about virtual world simulations, period.
  Position, orientation, etc of physical objects in a 3D world, mostly
What if we want different data in the PDUs? Or a new PDU? This requires a trip to the standards organization to define a new PDU
HLA changes this by making the set of data to be exchanged a configurable parameter of the simulation

## Slide 13: Configurable Simulation Data
This data is called the Federation Object Model, or FOM
  We can define a simulation that talks about objects in a 3D world with a FOM that has virtual world data such as position, orientation, and so on.
  We can define a simulation that talks about logistic center missile repair or discrete event simulation, like SimKit, that talks about time to repair, workstation, etc.
  We can define a simulation that talks about combat simulation that talks about Pk, weapons mix, etc.
The second two might not reference position and orientation at all
The set of data a given simulation might refer to is customized for application and called the FOM.

## Slide 14: Federation Object Model (FOM)
Logistic Repair FOM
3D World
FOM
Two simulations with two different FOMs for two different purposes

## Slide 15: FOM
Notice that if we have two different FOMs, then the simulation participants can’t talk to (exchange information with) each other.
There has to be semantic overlap of the FOMs, and even then it wouldn’t be easy. The concept of missile repair doesn’t necessarily map well to dynamic 3D worlds.
Just saying that two simulations use HLA does not mean they are compatible!!

## Slide 16: RPR FOM 1
There are a lot of simulations out there that do DIS semantics
  Entity Types
  Entity IDs
  Coordinate systems
Not just abstract idea of “position and orientation,” but all the way to specific meanings used in DIS.
If you’re trying to port your DIS application to HLA, well, why not use same semantics as DIS? They’re already well thought out and debugged…
So DIS actually presents us with an object model.
Notes: TODO how long did it take RPR-FOM to emerge? V1 and v2
DIS / RPR FOM PSG (sisostds.org)
https://www.sisostds.org/StandardsActivities/SupportGroups/DISRPRFOMPSG.aspx

## Slide 17: RPR FOM 2
This is the conceptual idea behind the Real-time Platform Reference Federation Object Model (RPR-FOM).
Simply uses DIS semantics in an HLA FOM.
This minimizes the changes necessary to the upper levels of the simulation’s logic.
Also lets DIS PDU packets exist “inside” models of a RPR-FOM HLA simulation.

## Slide 18: Simulation Clock
DIS runs in real time — wall clock time passes at the same rate as simulation time.
  When you fly an aircraft in DIS it doesn’t go faster or slower than wall clock time; the simulation user has the same perception of time as the real world.
In contrast, the missile repair simulation might model the repair operations over a weeks-long period. This is common in Discrete Event Simulation (DES) such as Simkit… TODO for NPS!
Typically it might be silly to run such event-based simulations at the same rate as a wall clock.

## Slide 19: Simulation Clock
HLA can optionally use a simulation clock.
Much like discrete event simulation (DES) event-queue timing, skip uneventful times.
The simulation clock advances only when all participants agree that it can be advanced.
For example a sim running on host A doesn’t advance its shared sim clock until all other hosts agree that clock can be advanced, based on what they expect in the simulation.

## Slide 20: HLA Versions
HLA has gone through several versions:
HLA was originally standardized by the Defense Modeling and Simulation Office (DMSO) and the final version of this branch was HLA 1.3
  HLA also entered the IEEE standards track and was standardized as IEEE 1516. This is considered the more current version
  STANAG 4603 can refer to both 1.3 and 1516
  HLA Evolved is the 1516 follow-on product
HLA 1.3 is still widely used. IEEE 1516 is used a fair amount. HLA evolved is still somewhat rare, with the vendor Pitch being the lead vendor, MaK also
Some free/open source implementations, mostly HLA 1.3

## Slide 21: HLA terms
Understanding HLA requires mastering some terminology first:
A federation is a related group of software components that cooperate with each other
A federate is one cooperating element in a federation
A federate execution is one run of a federation
Run Time Infrastructure (RTI) is the software that allows federates communicate with each other

## Slide 22: HLA
Federate A
Federate B
Federate C
Run-Time Infrastructure (RTI)

## Slide 23: HLA
One rule of HLA is that all federates must communicate federation information over the RTI. They can’t communicate federation data between federates in any other way.
Thus you can’t open a socket between two federates and exchange federate data over that channel.
(Exchanging non-federate data is still OK.)

## Slide 24: HLA Objects
What data do they communicate?
The precise data structures are defined by the shared Federation Object Model (FOM).
  Effectively, the interfaces to each object
“Object” is defined a little differently than in programming languages. In HLA, an object describes only the data fields--there are no methods associated with objects.
Objects have attributes describing their characteristics.

## Slide 25: HLA Objects
Vehicle
(serial number)
Tank
(serial number)
(Rounds main gun)
Truck
(serial number)
(Gallons gas)
Objects are defined in the FOM and have attributes
that they may inherit in an inheritance hierarchy,
but no methods are directly defined.

## Slide 26: FOM
Each FOM describes
  All public object classes that can be shared (communicated) between federates.
  Specification of all object attributes for classes.
  All interaction types (events) and their parameters.
This is federation-wide, i.e. all objects and interactions that can exist in a federation.

## Slide 27: FOM & RTI
The FOM is provided to the RTI when the simulation starts. This defines the messages that can be passed between federates.
The FOM defines what can be passed; the RTI provides the infrastructure to pass it.
The RTI is also responsible for exposing functionality like time management and simulation management.

## Slide 28: Time Management
“Real time” simulations such as DIS don’t have much of a concept of simulation time distinct from wall clock time--everything just happens as packets arrive from the network.
But different types of simulations might need to manage time differently: discrete event simulations, time-stepped simulations, faster than real time simulations, etc.
HLA provides services to manage timing.

## Slide 29: FOM
A FOM includes
  an enumerated listing of all public classes,
  description of all interaction types and parameters, and
  specification of all attributes that characterize public objects.
Thus it provides “object types in the world that the federations can talk about”, more or less

## Slide 30: Object Ownership
Federates “own” objects or attributes of objects.
For example, we can create a tank object and assign ownership of the object to one of the federates. That federate has authoritative information about that tank object, and sends updates to other federates when the tank attributes change.
Other federates can subscribe to the object or object attributes, which means they are sent updates.
Objects and attributes can also have their ownership passed to another federate.
Thus a convenient modeling framework is provided for distributed large-scale object management.

## Slide 31: Federates & Objects
Federate A
Federate B
Federate C
RTI
Tank A
(gun rounds = 15)
Tank A
(gun rounds = 15)
Object attribute
update sent
via RTI to all federates
that are subscribed

## Slide 32: Simulation Object Model (SOM) SOM, FOM
The Simulation Object Model (SOM) defines the data that an individual federate shares with a federation. This may be a subset of the FOM.
The FOM may define tanks, helos, and IFVs. Meanwhile a SOM for one federate might define only tanks.
The FOM is a subset of the union of the SOMs (separate entities might be handled by each sim).
In the case of RPR-FOM, it seems that most federates simply adopt the RPR-FOM as the SOM.

## Slide 33: HLA components
Object attributes are owned by federates.
Federates cooperate in a federation.
Federate execution is one single distributed running simulation.

## Slide 34: Object Model Template (OMT)
The OMT is HLA’s way of describing and defining objects
  Programming-language (vendor) neutral
  Object-class structure tables
  Interaction-class structure tables
  Attribute tables
  Parameter tables

## Slide 35: Object Management Table (OMT)

## Slide 36: OMT
Roughly speaking: object classes are permanent, while interaction classes are used only for transferring information and have an “instantaneous” lifespan. Interaction classes are essentially events.
Attributes are associated with each class definition.
Objects: entities in the world that have some time duration lifespan
Interactions: events, typically zero time duration
The FOM and SOM are defined using the OMT, a technique for formalizing the structure of classes and interactions

## Slide 37: Management Object Model
The MOM provides a way to learn about the federation. Essentially, this is the FOM for RTI; the same mechanism is used to interact with the federation execution as is used to interact with other federates.
  Federation execution operating information
  Operations of joined federates and RTI
  Control of the RTI and federates

## Slide 38: Distributed Data Management
DDM refers to area of interest management (AOIM) which is handled via the RTI
“Only distribute information about this class to federates who are interested in this geographic region”
Another look at AOIM: Michael Macedonia, A network software architecture for large scale virtual environments, NPS dissertation, 1995. (Hexagon basis vice squares.)

## Slide 39: HLA Rules, 1-4
HLA has ten basic rules that are actually general.
  Federations shall have an HLA Federation Object Model (FOM), documented in accordance with the HLA Object Model Template (OMT).
  In a federation, all representation of objects in the FOM shall be in the federates, not in the run-time infrastructure (RTI).
  During federation execution, all exchange of FOM data among federates shall occur via the RTI.
  During a federation execution, federates shall interact with the run-time infrastructure (RTI) in accordance with the HLA interface specification.

## Slide 40: HLA Rules, 5-7
  During a federation execution, an attribute of an instance of an object shall be owned by only one federate at any given time
  Federates shall have an HLA Simulation Object Model (SOM), documented in accordance with the HLA Object Model Template (OMT) (single federate)
  Federates shall be able to update and/or reflect any attributes of objects in their SOM and send and/or receive SOM object interactions externally, as specified in their SOM.

## Slide 41: HLA Rules, 8-10
  Federates shall be able to transfer and/or accept ownership of an attribute dynamically during a federation execution, as specified in their SOM.
  Federates shall be able to vary the conditions under which they provide updates of attributes of objects, as specified in their SOM
  Federates shall be able to manage local time in a way that will allow them to coordinate data exchange with other members of a federation.

## Slide 42: APIs
Note that HLA does NOT specify the format of the data interchanges on the network wire. Thus different RTIs from different vendors can use completely different formats, not interoperably.
So what actually is standardized?
  The OMT and FOM/SOM specifies the object model --you should be able to carry these between RTIs.
  HLA standard also includes standardized APIs for the “RTI Ambassador” and “Federate Ambassador”, which is interface of the federate to the RTI (and vice versa).

## Slide 43: Ambassadors
Federate
RTI
Ambassador
Federate
Ambassador
RTI

## Slide 44: Ambassadors
The federate (your code) talks to the RTI via the RTI ambassador.
If the RTI must talk to your code, it does so by executing “callbacks” in your code initiated by the federate ambassador.
These APIs and protocol handshakes are standardized.
This means you can take your federate code to an RTI from another vendor and (modulo version issues) have it run.

## Slide 45: Another Cycle
Take another trip through the description:
  HLA Rules
  HLA federates, federation executions, RTIs, ambassadors, and objects
  Reflection of object attributes
  Ownership and ownership transfer

## Slide 46: FEDEP
Federation Development and Execution Process (FEDEP) is a standardized methodology for developing HLA simulations.
The FEDEP is distributed as an IEEE standard in itself.

## Slide 47: HLA Vendors
There are several vendors out there:
Pitch: www.pitch.se Probably the most “modern”; deeply involved in the latest rev, HLA-Evolved
MaK: http://www.mak.com Widely used; big user base from the HLA 1.3 days, promises to be compliant with the latest revs
Portico: https://www.porticoproject.org Open source, java-based RTI; some support from the Australian MoD
CERTI: https://github.com/etopzone/CERTI
There is an RTI certification process (which not all RTIs have been through)
Notes: http://www.cert.fr/CERTI is former site

## Slide 48: HLA Resources
CSU Chico has a good set of slides:
  https://www.ecst.csuchico.edu/~hla/courses.html#module1
  https://www.ecst.csuchico.edu/~hla/courses.html#module2
Books:
  Creating Computer Simulation Systems: An Introduction to the High Level Architecture, Kuhl, Weatherly, & Dahmann, 1999.
  Guide to Distributed Simulation with HLA, Okan Topçu, Halit Oğuztüzün, 2017
Wikipedia:
  High Level Architecture

## Slide 49: HLA controversy: actual standard?
… definitely exists, continued for many years
Standards are based on interoperability
HLA might just be the only “standard” that does not include interoperability
More on this can be found on Wikipedia’s Talk tab discussing page design… see “Definition of terms: standardized protocols support interoperable data exchange”
Caveat emptor. You have been advised!
Notes: Definition of terms: standardized protocols support interoperable data exchange
Standards are designed to achieve interoperability. Indeed the very name of Simulation Interoperability Standards Organization (SISO) includes "Interoperability" in its title. There are three definitions given for interoperability on Wiktionary:
The capability of a product or system to interact and function with others.
(military) The capacity for a service, piece of equipment etc., to be operated by different forces or groups.
(computing) The ability of software systems that may be running under different operating systems and hardware to exchange information through compliance with technical interoperability specifications, which typically define how different file formats and messaging protocols can work together.
Similarly in Wiktionary the ninth (computing) definition for protocol states "A set of formal rules describing how to transmit or exchange data, especially across a network."
Contrary definitions regarding RTI have caused a lot of misunderstanding. It is simply contradictory to claim that an RTI implementation supports a standardized protocol if interoperable data exchange is not provided.
Don Brutzman (talk) 20:24, 14 February 2013

## Slide 50: Definition of terms: standardized protocols support interoperable data exchange
Standards are designed to achieve interoperability. Indeed the very name of Simulation Interoperability Standards Organization (SISO) includes "Interoperability" in its title. There are three definitions given for interoperability on Wiktionary:
  The capability of a product or system to interact and function with others.
  (military) The capacity for a service, piece of equipment etc., to be operated by different forces or groups.
  (computing) The ability of software systems that may be running under different operating systems and hardware to exchange information through compliance with technical interoperability specifications, which typically define how different file formats and messaging protocols can work together.
Similarly in Wiktionary the ninth (computing) definition for protocol states "A set of formal rules describing how to transmit or exchange data, especially across a network."
Contrary definitions regarding RTI have caused a lot of misunderstanding. It is simply contradictory to claim that an RTI implementation supports a standardized protocol if interoperable data exchange is not provided.

## Slide 51: response: Indeed by LVCTaylor
The concept of “Interoperability” has never been so mangled and redefined as it has been under banner of HLA. SISO has seen more than one attempt to change its name to remove or replace the word “Interoperability” to avoid such a prominent display of SISO’s purpose. I know of at least two excellent systems architects who left SISO partly for this very reason who know fully well what the HLA is and why it should never be used where the word “interoperable” is important.
One has to ask a simple question when designing DM&S applications: Do I expect anyone to interconnect to this application in the future that might not use the same RTI? If the answer is yes, then don’t force the other sides to PURCHASE the same middleware, or for that matter, don’t use it at all and find another means to interconnect the applications.