## Slide 1
Distributed Interactive Simulation (DIS) 101: The Basics
Don Brutzman, Terry Norbraten and Chris Fitzpatrick
Modeling, Virtual Environments, Simulation (MOVES) Institute
Naval Postgraduate School (NPS), Monterey California USA
brutzman@nps.edu tdnorbra@nps.edu christian.fitzpatrick@nps.edu
Notes: Note that this tutorial is essential to core design of current Modeling and Simulation architectures. It complements I/ITSEC tutorials on Test and Training Enabling Architecture (TENA) and High Level Architecture (HLA).
Intended Audience. Practitioners interested in networking, simulation interoperability and shared virtual environments using open standards.
Abstract. The Distributed Interactive Simulation (DIS) protocol is a well-established IEEE standard for packet-level exchange of state information between entities in military simulations. DIS facilitates simulation interoperability through a consistent over-the-wire format for information, widely agreed upon constant enumeration values, and community-consensus semantics. Anyone can obtain the IEEE-1278 standard and implement their own compliant, interoperable, DIS application. A large variety of tools and codebases simplify this effort, and enable multi-architecture integration of simulations using the DIS stand baseline. DIS focus begins with real-time, physics-based, entity-scale simulations, providing state update and interaction mechanisms which can scale to large virtual environments. This tutorial is a "DIS 101" introduction for software implementers and an introduction to the DIS philosophy for simulation systems integrators. Examples are provided using the open-source Open-DIS library for DISv7 and Enumerations support, available in multiple programming languages. Ongoing work is included in unit testing of DIS streams, and Web-based implementations using X3D Graphics, as well as Compressed DIS and DISv8 development.
Grateful acknowledgement: this tutorial was originally developed by Don McGregor NPS.

## Slide 2: Learning Objectives
The learner will be able to…
Identify what standards are used by distributed simulations for military use.
Identify what types of communication protocols are used for various networks.
Identify what aspects needs to be standardized, and what aspects can be customized, to support diverse simulations with differing models and goals.
Identify how DIS techniques for dead reckoning (DR), visual smoothing and distributed collision detection can reduce network traffic.
Learn prospects for new capabilities expected in Compressed DIS and DISv8.
Notes: Discuss how connecting all manner of simulations, namely Live Virtual Constructive LVC, is the necessary path for connecting to Command and Control (C2) systems. Establishing such connections between traditionally separate domains is central to conference theme,
“The Future is Now“
Note that, for example, common tutorial topic “What coordinate systems are used?” is also central to requirements for connecting C2 and M+S.
Slide 2 and last slide are identical.

## Slide 3: Topics
What is distributed simulation? Scaling from isolated networks to the Web.
Military modeling & simulation, distributed simulation standards, interoperability
Underlying TCP/IP network requirements common to all distributed simulations
DIS: goals, design principles, basic structure, Entity State PDUs explained
DIS: distributed identification of all participants, Entity Types and Entity IDs
DIS: tracks and Coordinate Systems, real time clocks, packet PDUS, code APIs
DIS: collisions, shooting, Dead Reckoning, Smoothing, visual synchronization
DIS and Open-DIS: DIS standard development, ongoing implementation efforts
Resources and References for further activity, including latest software builds
Notes: Communicate that this is a broad and deep topic. Much information is available. Ace card for participants: DIS “just works” across many systems, is much tested and strives to match/represent real-world activities. So experience in each domain being simulated is useful.

## Slide 4: Distributed Simulation Terms
A distributed simulation runs on multiple cooperating hosts on the network.
State information describes the position, orientation, and other information about an entity at a point in time.
Live, Virtual, Constructive (LVC) simulation involves different hosts doing different aspects of simulation in one cooperative system.
  Live: Real people, real systems
  Virtual: Real people, simulated systems (human in loop)
  Constructive: simulated people, simulated systems (AI controlled)
Notes: Emphasize that terminological clarity is always important when modeling cross-domain interactions.

## Slide 5: Live, Virtual, Constructive (LVC) Example
Automatic Identification System (AIS) is a standard for transmitting the current position of commercial ships in the real world; ships have a transmitter and receiver on board and send information in a standard format. This is a live component (real system, real people).
Ship simulators portray a simulated virtual view of navigation from the perspective of a ship’s bridge, perhaps in a “cave” environment with wall-sized screens. This is a virtual component (real people, simulated system).
We can also inject simulated, computer-generated ships controlled by AI into the simulation. This is a constructive component (simulated system controlled by simulated people).
As LVC connects M+S with C2 for warfighters, ever-greater synergies emerge.
Notes: Stress final point, encourage participants to consider LVC in their individual domains of interest.

## Slide 6: Live, Virtual, Constructive (LVC) Example, Illustrated
Participants may be local or distributed
Virtual: bridge simulator
Live: AIS feed
Single
Shared LVC
Environment
Constructive: computer-
generated ship traffic, controlled by AI agents
Notes: This diagram is not showing “one way to do things,” rather many alternative variations are possible depending on scenarios of interest.

## Slide 7: What Do We Want to Do?
DIS has been running and evolving since early 1990s, remains widely used in many applications.
People who want to learn about Distributed Interactive Simulation (DIS) usually are in the “virtual” or “constructive” domains, though it can also be used in the live domain.
  They want to simulate ships, tanks or other entities in 3D world, controlled by humans or AI.
We need to exchange state information between hosts on the network about entities in the world.
  To view someone else in the simulation, we need to know their position, orientation, and other state information, and this information needs to be sent to us by them.
Typically entities are controlled by different hosts that are connected via a network. The state information is usually exchanged over the TCP/IP protocol.
Notes: Shared state is the essence of a distributed virtual environment. If participants can’t communicate well, then they can’t interact well.

## Slide 8: State Information in Distributed Simulations
State Information
Location, Orientation, Velocity, etc of Entities
Sent over a TCP/IP network
Tank Simulator
Helicopter Simulator
Notes: The tank & helicopter in the simulation are controlled by different hosts. The simulation running the tank needs to know about the helicopter’s position, and the helicopter needs to know about the tank’s position
We have to come to all sorts of agreements to exchange information. It’s harder than it looks!
We want the information to be in a standard format, because we don’t want to be locked into one vendor

## Slide 9: What’s So Hard About That?
The format of state update messages needs to be exactly specified.
  What coordinate system should you use? You need one that works well for ground and air systems, and can handle curvature of the earth issues.
  Text or binary format messages?
  The order in which the fields appear?
Network issues: what happens if a message is dropped?
Scalability issues: how can we get a reasonable number of entities to participate?
Latency: can we keep the message delay reasonable?
Do all participants have a consistent, coherent operational picture?
Notes: Convey that all of this complexity must be handled sensibly and sharably, which is design basis of DIS.

## Slide 10: Distributed Simulation Standards
There are many ways to exchange the state information, but we want a standard way so we can interoperate with simulations from many vendors rather than being locked in to one. We don’t want to use only one vendor’s proprietary method, for which we will pay dearly.
In the case of defense modeling and simulation, the “big three” are
  TENA: Test and Training Enabling Architecture
  HLA: High Level Architecture
  DIS: Distributed Interactive Simulation
TENA and HLA include many semantic concepts borrowed from DIS. Understanding DIS has carry-over benefits when working with other standards.
Notes: Stable interoperability is essential for long-term use, re-use, sharing and advancing progress.

## Slide 11: State Information Exchange Standards
Controlling Host
Receiving Host
DIS
HLA
TENA
The controlling host sends the state information update
via one of the standards to other hosts
State Information Updates
Notes: As ever, consistent syntax and semantics are both required if senders and receivers are going to achieve shared understanding of context and consistent, coherent interactions.

## Slide 12: TENA
Used on ranges; often the “L” in Live-Virtual-Constructive simulations.
Designed for real time and embedded systems, real sensor systems, etc.
In effect it is thinly disguised CORBA distributed objects with multiple new features to help it work in a simulation environment.
Can gateway it to other standards, such as DIS or HLA.
See http://tena-sda.org
Notes: Encourage participation in all three tutorials, they are complementary

## Slide 13: High Level Architecture (HLA)
HLA is very general and intended to cover most defense modeling domains including training, analysis, and engineering in addition to virtual worlds.
Participants communicate via an agreed-upon Federation Object Model (FOM) and an API associated with a Run-Time Infrastructure (RTI).
Specification is maintained by SISO (http://sisostds.org), is IEEE standard 1516 and has implementations by
  MAK (http://www.mak.com),
  Pitch (http://www.pitch.se),
  Portico (older version) (http://porticoproject.org) and others.
http://www.pitch.se/hlatutorial is a good introduction to HLA.
Notes: Encourage participation in all three tutorials, they are complementary

## Slide 14: Distributed Interactive Simulation (DIS)
DIS was the first standard to tackle these problems in a systematic way.
Originated in the SIMNET project in the 80’s. DARPA supported converting the SIMNET research into a standard; SISO developed the standard and took it to IEEE for formal approval.
Anyone can get standard from IEEE, implement it, and participate in simulation.
Development of standard continues; updated DIS standard version 7 is the latest approved version. SISO maintains DIS, presents it to IEEE for approval.
Substantial commercial support, open source implementations, many home grown implementations of portions of the standard.
Notes: Encourage participation in all three tutorials, they are complementary

## Slide 15: Distributed Interactive Simulation (DIS) functionality
What does DIS support?
  A standardized way to exchange messages about entities in a shared distributed virtual world
  Common semantics for coordinate systems and other information, such as how to describe and specify entities
  Common practices to ensure interoperability among simulations
Notes: Essentials. All the detail flows from these design principles. Meaningful results are not otherwise possible.

## Slide 16: Networking: the Protocol Stack
DIS defines the format of the messages, but doesn’t specify how to get the messages from one host to another. Almost always this is done via TCP/IP network protocol.
Knowing network basics helps you be a better simulation designer/user!
DIS software libraries
Message passing
between hosts:
TCP/IP protocol, implemented by
each host machine’s operating system
Link and Physical
IP
TCP Sockets
Application
UDP Sockets
Notes: TCP/IP is the underlying substrate for almost all network communications. Web servers, streaming video, email and almost everything else you use on the internet all rely on TCP/IP
Users typically implement things at the “application layer” at the top of the stack. This is where DIS lives
  Somewhat confusingly, the DIS protocol is considered part of the “application layer” in addition to what users think of as the “application”, the visual simulation
The lower layers of the stack are responsible for delivering messages. We can usually ignore this part; it’s all handled by operating system vendors
We interact with the TCP/IP stack via either the User Datagram Protocol (UDP) or Transmission Control Protocol (TCP) APIs.
UDP messages are like postcards: they contain a fairly small amount of data, and we need to address them to a destination
  We can send them to one host (based on IP number): called unicast
  We can send them to all hosts on a local network: called broadcast
  We can send them to those hosts, on the local network or not, that are interested in the message: called multicast
DIS messages are contained inside of UDP packets and can use any one of these addressing schemes. Broadcast is very common. Multicast is better.

## Slide 17: TCP/IP and UDP
TCP sockets have higher latency, higher jitter (variation in latency), and doesn’t scale to large numbers of hosts as well.
UDP sockets have lower latency, lower jitter, scales to large numbers of participants better, but are unreliable.
DIS typically uses UDP.
Hold on—UDP is unreliable? What’s up with that?
  Individual UDP messages may be dropped by the network; there’s no guarantee that each UDP message will be delivered. This tradeoff achieves lower latency and jitter, which in turn brings better scalability.
  Not as big a deal as it might seem. If we get position updates from entity every 1/30th of a second, does it matter if we drop one? Better information is coming along shortly, so why resend dropped messages?
Notes: In some ways TCP/UDP are yin/yang of networking. Helping participants understand this point helps them comprehend many other DIS design decisions.

## Slide 18: DIS Messages
We know what we want to do: send a message that tells another host what the state of an entity is.
We know how we do this: send the message via TCP/IP, typically in a UDP message over broadcast or multicast.
What is actual format of the messages? This is specified by the DIS standard.
  There are dozens of possible messages to send, relating to everything from logistics to electronic warfare to radio communications.
  Each message type is called a “Protocol Data Unit” (PDU).
Notes: PDUs are messages. So are email, SMS text, 2-way web-browser interactions, and even object-oriented method invocations.

## Slide 19: DIS Messages
PDU
Entity Information
Entity State
Collision
Warfare
Fire
Detonate
…
Several dozen different message types (called Protocol Data
Units, or PDUs) to describe entity movement, collisions,
combat, radio communications, logistics, and many more.
The Entity State PDU is the most widely used.
Notes: The world is a big place, many years of work by M+S community have established a rich vocabulary of messages supporting modeling and information sharing that reflects the real world.

## Slide 20: PDU Families are Diverse
Credit: from SISO slideset
IEEE 1278 Distributed Interactive Simulation (DIS) by Mark McCall and Bob Murray, 26 May 2010.
Now all stably defined.
Many people have used and extended DIS Protocol so you can likely find what your system needs to do.
Notes: Ask participants if they have knowledge of any of these domains.

## Slide 21: DIS Messages: Entity State PDU
We use ESPDU when want to inform other hosts of the position of an entity we control—the most common PDU
Entity sends ESPDU with
• Unique ID
• Position (xyz) in standard coordinate system
• Orientation
• What type of vehicle it is
• More….
Notes: ESPDU is workhorse PDU, and also affects how other PDUs are interpreted.

## Slide 22: Site, Application, Entity ID: a Unique Identifier
Before telling entities “hey you there, do that” we need a way to differentiate between entities.
The entity ID is a unique identifier for each simulation object in the world. In DIS this is accomplished via a triplet of three numbers: Site, Application, and Entity ID numbers.
This triplet of three numbers taken together must be unique for each entity.
Notes: Interesting that three-valued ID can scale across multiple levels of interaction: local, deliberately shared, and globally unique.

## Slide 23: DIS: Entity IDs
Example: before the simulation starts we agree, simulation-wide, on the following arbitrary numbers. Here are simple possibilities:
Site | Number
China Lake | 42
Norfolk | 17
Orlando | 23
Application | Number
YoYoDyne M1A2 Simulator | 112
ACME UCAV Simulator | 417
JCATS | 512
Notes: This might seem simplistic but, essentially, the actual approach in larger simulations isn’t much different.

## Slide 24: Entity IDs
Tank Simulator
EID: (42, 112, 18)
EID: (42, 112, 19)
Helicopter
EID: (17, 417, 18)
ACME (417) simulator at
Norfolk (17) controls a
Helicopter (entity 18)
YoYoDyne simulator (112) at
China Lake (42) controls two
distinct tanks, 18 and 19
Notes: Aha moment: triples designate “who” sent a PDU and can identify any participant uniquely.

## Slide 25: DIS: Entity Type
We may need some other information. What if we want to draw this entity? We need to know what kind of entity this is—a tank, a helicopter, a ship?
This is done via a field called the Entity Type, which in turn depends on a SISO document called the “Enumeration and Bit Encoded Values” (EBV).
The EBV document is a long listing of standardized record values that lets us identify military hardware.
Notes: Designates “what” kind of thing this entity is.

## Slide 26: Entity Type
{
Kind: 1 (entity)
Domain: 1 (Land)
Country: 225 (US)
Category: 1 (Tank)
Subcategory:1 (M1)
Specific: 6 (M1A2)
}
Whenever a DIS message has an entity type record with the above settings
we know it’s referring to an M1A2 tank. What the numbers are doesn’t matter, as long as all participants agree on what they mean. SISO maintains the master list of arbitrary numbers, called the EBV document.
Notes: Subcategories flesh out the details and variations corresponding to each entity type.

## Slide 27: Entity Type From EBV Document
Notes: Note this community has met for years. EBV values available in Word, XML and derivative forms.

## Slide 28: Entity Type
The EBV document has gone through many versions as new hardware has been added. An important checkpoint for consistency: all participants in the simulation should agree on the current version of EBV document being used.
In reality this can sometimes be hard; some simulations have not been updated to reflect new EBV documents, and sometimes those implementing a simulation simply make up numbers, and no simulation implements all entities in the EBV.
You may need a gateway such as Joint Simulation Bus (JBUS) to act as a “shim” connection between simulations and change entity type values to match what is expected. The gateway can rewrite the entity type values in the PDUs to force them to match expectations.
The EBV enumerations are also often used in HLA RPR-FOM and in TENA.
Notes: Note that EBV for Entity Type goes to great pains to maintain backwards compatibility, so almost everything stays stable over time.

## Slide 29: Entity State PDU: Position
What does it mean if we say an entity is at (x, y, z)? This has no meaning without a coordinate system. We need to agree on one, and where the origin is.
DIS chose to use a Cartesian, geocentric coordinate system because
It’s easy to convert from that to other coordinate systems, such as geodetic
(latitude, longitude, altitude) or military
Systems such as MGRS.
Notes: If you want to specify the location of an entity in DIS, you have to specify it in terms of how far from the center of the earth it is. You should also agree on the shape of the earth (eg WGS-84) and terrain.
Using geocentric coordinates may seem strange, but DIS has to account for curvature of the earth issues if the simulation demands it. The geospatial people have done the math to convert geocentric coordinates to latitude, longitude, altitude, MGRS, or other coordinate systems. The geocentric coordinate system is often used in TENA and HLA
SEDRIS has provided an open source framework for dealing with these issues in their Spatial Reference Model (http://www.sedris.org/hdr1trpl.htm)

## Slide 30: DIS: Coordinate Systems
Very often simulations set up a local, flat-plane coordinate system at a point tangent to a point on the earth’s surface, using that for local physics movement.
When ESPDU is actually sent, local coordinates are changed back to the global coordinate system. The SEDRIS SRM package can do all the math.
Nobody will ever agree on one single way for local coordinate system axes to point identically for all simulations. YMMV !
Notes: Utility methods for conversions are how codebases comply and cooperate.

## Slide 31: Coordinate Systems
A local Cartesian coordinate system origin is set at {lat, lon, alt}. The simulation
does all calculations and movement in this coordinate system, because it’s convenient. Before sending entity information out in a DIS ESPDU, convert from local to geocentric (DIS) coordinates:
Local coordinate system origin
At lat 43.21, lon 78.12, alt 120m, WGS 84
X
X (East)
y (North)
Entity position can be expressed in:
Local: (10, 10, 4)
Geodetic: 43.21001 N, 78.12012W, 124
UTM: Zone 44N, 266061E, 4788172N, 124M
DIS: 958506.1, 455637.2, 4344627.4
We have enough information to convert
from one coordinate system to another,
if local coordinate system origin known.
Notes: (Ensure participants understand these simple concepts.)

## Slide 32: DIS: Dead Reckoning (DR) Algorithms
If we’re running a visual simulation, how often do we need to send ESPDUs?
If running at frame rate, maybe about every 1/30th of a second.
  If we have 500 entities in a simulation, this works out to 15,000 UDP messages per second. If you’re doing other computation on host, this will tax your CPU and network.
Do we really need to send that fast? If we know how fast and in what direction an entity is moving, we can “dead reckon” in between receiving each ESPDU and then interpolate position to draw our entity there.
  Sure, we’re lying to the user. Got a problem with that? If our DR is wrong, we just correct our position stealthily when we get better info on the next packet. The user won’t know the difference, probably.
  Due to latency all simulation participants are a little out of sync anyway.
Notes: This is applying relatively simple math to everyday physics. This is conceptual similar to how people fly, sail and drive.

## Slide 33: DIS: keeping it real, with less throughput required
Dead Reckoning (DR) algorithms use projected trajectory information (such as linear or rotational velocities and accelerations to compute how often network updates need to be sent. Helpful for quiet and intensely active intervals.
Visual smoothing techniques hide when packets are dropped or arrive late. Entity display smoothly interpolates to the correct location and direction, avoiding distracting jumps that do not correctly represent behavior anyway.
Having each individual entity honorably compute whether collisions occurred takes advantage of highest fidelity information with least computation, avoiding expensive time delays and greater inaccuracies of server-based adjudications.
Notes: No single optimization is possible. This is a tradeoff so that DIS can meet the shared expectations of participants.

## Slide 34: Dead Reckoning (DR) Example: Shared Track Fidelity
Green Line: “Truth” Track Model (physics-based Sender)
Red Line: Dead Reckoned (extrapolated) Track Model
(computed by Sender, used by Receivers)
White Line: Smoothing Algorithm (viewed by Receivers)
DR algorithms can include linear, rotational velocities/accelerations
ESPDU update rates by Sender are error sensitive
Notes: Senders have best state information so they are logical source of “ground truth”, this balance leads to best-case fidelity for shared track data.
Thanks to Mark McCall and Bob Murray for earlier versions of this slide.

## Slide 35: DIS: Timing and Dead Reckoning between ESPDU Updates
Time
ESPDU Updates
Aircraft position & orientation updated by dead reckoning updates between ESPDU messages
ESPDU 2
ESPDU 3
DR updates
Notes: High-order handwaving! Walk through a maneuver, describe what happens from each participant’s perspective. Emphasis here is timing.

## Slide 36: DIS: Dead Reckoning Algorithms and Updates
Which velocity-acceleration DR algorithm is best? (… wait for it…)
It depends! In some situations we might want to include acceleration or angular velocity, but not in others. Typically the information available varies. ESPDU senders specify what DR algorithm to use.
The sender can also perform its own internal DR to determine what each recipient is seeing. If sender sees that clients are probably wrong in their guess about where the entity is, based on accumulated error, sender can issue another ESPDU sooner with better state information.
Notes: George Box: “All models are wrong, some are useful.”

## Slide 37: DIS Dead Reckoning (DR) Smoothing, Synchronization
Dead Reckoning (DR) is projection of entity location based on last received timestamp, position and vector-based velocities/accelerations.
  Enables recipients to more accurately estimate entity state in-between PDU updates.
  Enables senders to more accurately estimate when to send more-frequent updates.
Smoothing is a recipient-presentation technique for handling dropped packets.
  Avoid sudden jerky jumps in motion, instead interpolate from prior estimate to new state.
  No need to improperly distract user with corrective actions when recovery is satisfactory.
Synchronization among multiple players is a blend of capabilities.
  Networking monitoring and management, simulation management, logging, etc.
  Measurable metric: is a “fair fight” taking place among distributed participants?
  Sometimes called “Triangle of Death: faster – better – cheaper, pick any two”
Notes: Hitting the “sweet spot” of where physics, math, networking, modeling, simulation, perception and reality align acceptably.
“Triangle of death” means that a perfectly optimal balance is not possible, must choose best cases within these tradeoffs.

## Slide 38: DIS: Learning About the World and Heartbeat
If we run a DIS simulation, how do we learn about all other entities in the world?
  One design possibility is to use a master server. Instead, the designers chose for DIS to be peer-to-peer; there is no central server, and hosts talk to one another directly.
In DIS essentially all we have to do is listen for ESPDUs. New-entity ESPDUs contain what we need to know: entity type, location, velocity, orientation. This is simple and avoids a single point of failure, making configuration easier.
  There are also Simulation Management PDUs for announcing arrival, removal, etc.
To make this work, every entity must periodically send a time-stamped ESPDU even if its state hasn’t changed. This is called a heartbeat. Usually entities must send an ESPDU at least once every five seconds.
Notes: Discovery of new entities, confirmation of known entities, learning of lost entities.

## Slide 39: DIS: Timestamp
One of the oddities of UDP is that UDP packets may be duplicated during TCP/IP routing; we send a single packet, but two might arrive nevertheless.
UDP packets may also arrive out of order. We send packets in order A, B, C, but they arrive in order C, A, B ....
  This creates problems for position updates! How to handle? ....
DIS includes a timestamp field to detect these kinds of problems:
  The field typically represents time since the top of the hour (as common practice).
  If the next packet we receive has a timestamp before the last packet we processed, then we can discard it; it’s old information that has been obviated by new data.
  Time coordination between hosts is useful but not required.
Notes: Accurate shared time is a great benefit that helps DIS accurately model interactions occurring across the network.

## Slide 40: DIS: Timestamp
Host A sends 1 and then 2. Host B receives 2, and then 1.
We should discard 1, because we know it’s older than 2,
due to its older timestamp.
2
1
1
2
Notes: OMG the network isn’t perfect?? That is correct… this is an example of how we cope.
Note how DIS design turns a potential weakness into a robustness feature.

## Slide 41: DIS: Entity State PDU
So far we’ve looked at an ESPDU, which contains
  Entity ID
  Entity Type
  Position, orientation, velocity, etc.
  Specifies a DR algorithm for the receiver to use
  Timestamp
We’ve also seen that we need to agree upon a coordinate system, and agree on the enumerations that describe things like entity type.
Notes: But wait there’s more… a lot more.

## Slide 42: DIS: no approved Application Programming Interface (API) per se
DIS doesn’t have an API. This seems strange to people coming from HLA or TENA, but reflects common practice in networking protocols.
  The standardized part is the format of the messages on the wire. The standard is silent about how to programs can create or receive those messages.
  Different DIS vendors have different APIs, but all produce the same format messages. This is in contrast to HLA, which has a standard API, but is silent about the format of messages on the wire. As a result, different HLA RTI vendors usually use different message formats for exchanging information.
  TENA standardizes the API, and there is a single approved implementation of the RTI equivalent; this sidesteps the wire standard problem because there is only one approved equivalent of the RTI.
Notes: Theme to convey: vive la difference.

## Slide 43: DIS: Message Format Standardized
Vendor A API for DIS
Vendor B API for DIS
Vendor C API for DIS
Standard Format Messages
JCATS Sim Code
ACME Sim Code
ONE-SAF Sim Code
Network
Notes: Can we all just get along? Yes, with commonly understood messages.

## Slide 44: HLA: API Standardized
HLA RTI API
HLA RTI API
HLA RTI API
RTI Vendor-Specific Format Messages
JCATS
ACME Sim
ONE-SAF
Network
While the API is standard, implementations of HLA RTI API from different vendors are allowed to produce messages in different formats.
Notes: Can we all just get along? Yes, with commonly accessed federated object models.

## Slide 45: DIS: Application Programming Interfaces (APIs)
The implications of this are that while HLA has a standardized API, RTIs from different vendors can’t typically talk directly to each other. This makes changing vendors easy, but makes getting RTIs from different vendors talking to each other hard--you need to use a gateway. Caveat emptor, let buyer beware…
DIS in contrast makes changing vendors hard (since it involves changing the API your simulation code uses) but talking between vendors easy (since all the messages on the wire are in the same format)
  The lack of an API can help when using a variety programming languages, such as Objective-C, C#, Python, and JavaScript. Since there’s no official API, just make one up that fits your application’s programming language. As long as they produce standard messages on the wire, the API creating packets doesn’t affect anyone else.
Notes: Programmers need some kind of API to create and read PDUs. You may use any from a variety of software libraries (for example Open-DIS) but your PDU messaging mileage won’t vary.

## Slide 46: DIS: Protocol Data Unit (PDU) Formats
Remember, all this information is being sent in binary format in (typically) a UDP packet.
The exact format that an ESPDU must have on the wire is specified in the DIS standard. This includes byte order.
For example, the EntityID field starts 12 bytes into the ESPDU message, is in the order (site, application, entity), and each field entry is 16 bits long, in network byte order, and unsigned.
Notes: Attention to detail is necessary for the simulation plumbing to work properly. Pipes + water == network sockets + PDU messages.

## Slide 47: DIS: ESPDU Format
Notes: Theme to convey: be not afraid, the IEEE DIS specification explains everything well. Proof point is decades of interoperability by diverse participants.

## Slide 48: DIS: Looking at ESPDUs
What do ESPDUs look like? We can examine them on the network with a free tool called Wireshark, which can decode DIS packets
  http://www.wireshark.org
Remember, it’s the format of the messages on the wire that count. The DIS standard specifies the exact format of binary messages, and any tool that produces or consumes those messages is fine with DIS. How you create them (or consume them) is none of DIS’s business.
Notes: We are moving from theory to practice.

## Slide 49: Wireshark: Capture Packets
Notes: Describe wireshark’s immense generality, availability, capability. Viva open source!

## Slide 50: Wireshark: Decode Packets as DIS
Notes: Wireshark does DIS too.

## Slide 51: Wireshark: Examine DIS Packets
Notes: Drill down to any/every level of detail lets everyone know what is really happening/working (and also enables debugging occasional mysteries).

## Slide 52: DIS: Implementations
Format
  We know what information we want to send: entity type, entity ID, position, orientation, etc.
  We know what coordinate system we want to use.
  We know where to find arbitrary, agreed-upon enumeration identifier values—the EBV document.
  We know some PDU types: entity state PDU, etc.
How do we get the information into the format we want on the wire?
This is where DIS implementations come in.
Notes: Review checkpoint. We’ve covered a lot – everyone on board?

## Slide 53: DIS: Implementations
Where can you get a DIS implementation?
  Write your own (cough cough)
  Buy one. There are several commercial implementations and many have excellent support.
  Use an open source version—”free as in free puppy” (… but also includes freedom to fix)
    Open-DIS (https://github.com/open-dis - formerly http://open-dis.sourceforge.net)
      Java updated to full coverage of DIS7, planning work on C-DIS and DIS8
      Planning to regenerate C++, C#, Objective-C, JavaScript, Python in 2021
    KDIS (http://sourceforge.net/projects/kdis) C++ (active)
    Aquarius (http://sourceforge.net/projects/aquariusdispdu) C++ (retired)
    JDIS (http://sourceforge.net/projects/jdis) Java (inactive)
Notes: Have fun out there. Emphasize that Open-DIS strives for exact compliance, and errors (actual or perceived) can be fixed by the community.
Note current work to establish a DIS unit-test suite to confirm repeatability by software applications and API libraries.

## Slide 54: DIS: Sending PDU Packets
Remember, DIS has no official API. Every implementation is different. This example will use the Open-DIS API codebase. Implementation available at https://github.com/open-dis
Source code now at https://gitlab.nps.edu/Savage/NetworkedGraphicsMV3500
Examples may contain supporting libraries for additional independent things .
All code is BSD open-source license; nonviral, use any way you see fit.

## Slide 55: DIS: Send ESPDUs in Java
Notes: Typical code excerpt for sending, uses Open-DIS

## Slide 56: DIS: Send PDUs in Javascript
Can use HTML5 Browser geolocation and Javascript to send
DIS from a web page
Notes: Typical code excerpt for sending to a web browser, uses Open-DIS

## Slide 57: DIS: Receive PDUs in Java
Notes: Typical code excerpt for receiving, uses Open-DIS

## Slide 58: DIS Sending and Receiving PDUs
There are similar idioms for other languages such as C++, Objective-C (IOS/MacOS), JavaScript, Python, C# (Windows phone, Unity 3D)
  But only implemented in earlier versions of OpenDIS library, updates await
Note that this requires that you do a bit of socket programming, which TENA and HLA hide from you. Socket programming isn’t that bad…
Notes: Virtue of programming: you only have to get it right once!

## Slide 59: Visualizing DIS Data via Online Map using DISWebGateway
DISWebGateway running at
http://track.movesinstitute.org
  Java sender & receiver for DIS
  Can receive native DIS from existing DIS applications
  Web-based map that shows DIS entity locations
Code refurbishment in progress…
Notes: Exemplar demo. Server is being moved, will be ready for IITSEC (being updated for 2 classes at MOVES).

## Slide 60
Notes: A script moves entities around a GoogleMaps display by animating KML placemarks with DIS.

## Slide 61
Notes: A script moves entities around an OpenStreetMaps display by animating KML placemarks with DIS.

## Slide 62
Code refurbishment in progress…
Notes: An HTML web-page form is used to create and send DIS ESPDU stream, source-code script uses Open-DIS JavaScript library with HTML.

## Slide 63: DIS: Shoot at Something
We’ve been sending ESPDU messages back and forth, but there are dozens of other sorts of messages. What if we want to shoot at someone? What does this involve?
We can use a Fire PDU, which contains
  The entity ID of the shooter
  The entity ID of the target (if known)
  The type of munition being fired, fuse, quantity, etc. This is very similar to the entity type
  Enough information to compute the path of the munition (if desired)
Notes: We are now moving from sending/receiving to interacting.

## Slide 64: DIS: Shoot at Something, then…
The Detonation PDU usually follows a Fire PDU. It contains
  Location of detonation, shooter entity ID, target entity ID
  Fuse, munition type, and so on
When a Detonation PDU is received simulations assess and report damage to their own entities, not to others.
  This means simulations are on the “honor system” for determining their own damage; thus James T. Kirk can beat the unwinnable Kobayashi Maru scenario.
  Here is a harsh adjective to describe cheating in distributed scenarios: boring.
  For military simulations we are much more interested in strengths, vulnerabilities and possibilities that may occur in the real world. Thus cheating is also critically unhelpful.
  Trusted participants using trusted software suites also reduces the risk of cheating.
Notes: Shared state for collision dynamics is fundamental to many many virtual environment interactions: driving, shooting, sensing, tracking, etc. etc. etc.

## Slide 65: DIS Shooting
Fire! I’m entity (17, 23, 42), shooting
at entity (123, 7, 12) with a HEAT round
from (x, y, z)
Explosion! There’s an detonation of a HEAT
round at (x’, y’, z’).
All entities now assess the damage to themselves by the
Detonation at (x’, y’, z’)
Notes: Walk through an interaction.

## Slide 66: DIS: Arbitrary Data
You can also exchange arbitrary data between DIS simulation participants with the DataQuery and Data PDUs.
  Participant sends a DataQuery PDU addressed to another participant
  That participant responds with a Data PDU
The data itself is sent as “fixed variable datums” or “variable data datums”. Therefore it’s up to you to specify the exact format of these
Notes: A protocol is a handshake, carefully choreographed.

## Slide 67: DIS: Other messages
There are many other messages that can be used in DIS
  Electronic warfare
  Logistics
  Directed energy weapons
  Voice/Intercom
  Collisions
  Simulation management
  Data exchange
It’s a big topic! Many different “conversations” can occur among entities.
But the basics are constant: a standard format for exchanging state information, and each has well-defined semantics for consistent usage and interoperability.
Notes: Lots more can be said!

## Slide 68: DIS and Other Standards: HLA, TENA
How can DIS interoperate with HLA or TENA?
HLA Real-time Platform Reference Federation Object Model (RPR-FOM)
  Intentionally matches DIS, same entity types, same entity IDs and coordinate system, etc.
  HLA object model mapping makes transition from DIS to HLA easy and consistent
  Several gateways to translate between DIS and RPR-FOM. JBUS, AMIE, others
  Guidance, Rationale and Interoperability Modalities (GRIM) for RPR-FOM standard provides further rules and usage information.
  https://www.sisostds.org/productspublications/standards/sisostandards.aspx
TENA has generalized gateway functionality that can map TENA events to DIS and vice versa. It generally uses the same coordinate system, entity types, etc.
Notes: There is a large community of practitioners and programmers out there.

## Slide 69: DIS Research Topic: DIS in the Web Page
Websockets are a standard from IETF and W3C. The idea is to provide a direct Javascript-based TCP socket into a web page without having to use AJAX polling techniques. Widespread browser support.
JavaScript is a widely used language for dynamic web content.
  WebGL is JavaScript binding for OpenGL which allows us to use accelerated 3D graphics inside the web page.
  WebGL can be the substrate for higher level graphics standards such as Extensible 3D Graphics Standard (X3D).
Put all three together and you can implement a networked virtual environment in a web page.
Notes: Lots of work, slowly steadily progressing. Web technology provides the greatest possible footprint, either on big internet or private military networks.

## Slide 70: DIS Research Topic: 3D in the Web Page
Web Server
Network with
conventional
binary-format
DIS packets
Web pages with Javascript
WebGL scene updated by
DIS over a Websocket
Notes: For example: it has to be simple to be repeatable and reusable.

## Slide 71: DIS Research Topic: 3D in the Web Page
Notes: Demo. Server may change, details will be confirmed at IITSEC.

## Slide 72: Applied Research using WebLVC
Excellent combinations of WebGL/X3D, WebSockets, and fast JavaScript in the web browser have emerged in recent years.
  Open-DIS library can send DIS PDUs directly into a web browser.
SISO WebLVC Product Development Group (PDG)
  https://www.sisostds.org/StandardsActivities/DevelopmentGroups/WebLVCPDG.aspx
One of many examples: Virtual World Framework
  http://virtualworldframework.com and https://en.wikipedia.org/wiki/Virtual_world_framework
Active research topic… but no wide-scale “Ready Player One” arenas for DIS, yet
Notes: There is no one single way to do it! There are many ways… and more work to do. Participants have an important role to play.

## Slide 73: DIS Tutorial Summary
DIS applications exchange state information among distributed set of players.
Defines stable syntax and semantics for a series of binary-formatted messages, with each packet’s bytes, data representation and functionality exactly defined.
Different software APIs can implement the same “over the wire” data standard.
Applications focused on large-scale, high-fidelity, virtual / constructive simulations.
Common concepts: entity types, entity IDs, heartbeats, coordinate systems.
Notes: Are we clear? Remembering key points remaining constant among many details.

## Slide 74: Resources and References
SISO: http://sisostds.org
SISO DIS / RPR FOM Protocol Support Group: https://www.sisostds.org/StandardsActivities/SupportGroups.aspx
Open-DIS: https://github.com/open-dis and
SEDRIS SRM: http://sedris.org
Kdis: http://kdis.sourceforge.net
Wireshark: http://wireshark.org
X3D Graphics: http://www.web3d.org/x3d/what-x3d and http://x3dgraphics.com/slidesets
WebGL: http://www.khronos.org/webgl
WebLVC: https://www.sisostds.org/StandardsActivities/DevelopmentGroups.aspx
WebSockets: http://tools.ietf.org/html/rfc6455 , http://www.w3.org/TR/websockets
This tutorial and additional examples can be found at
https://gitlab.nps.edu/Savage/NetworkedGraphicsMV3500
https://github.com/open-dis/open-dis7-java
Notes: More references available online. This takes study and, of course, we learn most of all from actual practice. Questions welcome, the community learns together.

## Slide 75: TODO: lots of work in progress!
Much work is ongoing in DIS at NPS, and partnered open-source efforts are welcome.
Improved Java enumerations (over 22,000 values) regularly autogenerated,
Improved OpenDIS7 library, full coverage of all 72 PDUs, growing set of examples,
Thesis work to support unit testing of simulations via DIS streams and LVC connectivity including Extensible 3D Graphics (X3D) Standard now available,
Planned work in Compressed DIS (C-DIS) encoding and DIS version 8 standards.
XML Schema for DIS-XML, possibly DIS Ontology for Semantic Web.
Considering use of Data Format Description Language (DFDL) parsing/unparsing.
Considering creation of an OpenDIS-OpenC2SIM bridge for packet passing.
We look forward to steady tutorial, workshop and library improvements each year.

## Slide 76: Thesis of Interest: Live Virtual Constructive (LVC) Replay
Tobias Brennenstuhl, REPEATABLE UNIT TESTING OF DISTRIBUTED INTERACTIVE SIMULATION (DIS) PROTOCOL BEHAVIOR STREAMS USING WEB STANDARDS, Masters Thesis, June 2020. (online) (video)
Notes: Abstract. The IEEE Distributed Interactive Simulation (DIS) protocol is used for high-fidelity real-time information sharing among simulations and trainers across the entire international Modeling and Simulation (M&S) community. If archivally saved and replayed, DIS streams have the potential to become a valuable source of Big Data. The availability of archived prerecorded behavior streams for replay, adaptation, and analysis can benefit an immense variety of application areas. The computer science principle “a stream is a stream” indicates that data in motion is equivalent to data at rest. This characteristic can enable powerful capabilities for DIS.
This thesis presents prototypes to demonstrate how various forms of repeatability are key to gaining improved benefits from DIS stream analysis. Unit testing of DIS behavior streams allows confirmation of both repeatability and correctness when testing all manner of applications, exercises, simulations, and training sessions. A related use case is automated after-action review (AAR) from recorded DIS streams. This thesis also shows how a DIS stream is converted into autogenerated code that can animate an X3D Graphics model. Many obstacles were overcome during this work, and so various best practices are provided. Of note is that unit testing might even become a contract requirement for incrementally developing and stably maintaining Live Virtual Constructive (LVC) code bases. This progress provides many opportunities for future work.

## Slide 77: Learning Objectives
The learner will be able to…
Identify what standards are used by distributed simulations for military use.
Identify what types of communication protocols are used for various networks.
Identify what aspects needs to be standardized, and what aspects can be customized, to support diverse simulations with differing models and goals.
Identify how DIS techniques for dead reckoning (DR), visual smoothing and distributed collision detection can reduce network traffic.
Learn prospects for new capabilities expected in Compressed DIS and DISv8.
Notes: Discuss how connecting all manner of simulations, namely Live Virtual Constructive LVC, is the necessary path for connecting to Command and Control (C2) systems. Establishing such connections between traditionally separate domains is central to conference theme,
“The Future is Now“
Note that, for example, common tutorial topic “What coordinate systems are used?” is also central to requirements for connecting C2 and M+S.
Slide 2 and last slide are identical.