## Slide 1: TCP/IP
Transmission Control Protocol, Internet Protocol (TCP/IP): The Universal Substrate
brutzman@nps.edu
Notes: Acknowledgement: original slides by Don McGregor

## Slide 2: Background
You’ve got some computers, each running a simulation. How do you get them to talk to each other?
Network

## Slide 3: Network Communications
“Almost” everything these days is done over TCP/IP, a framework for communications between devices
Note that TCP/IP is a software concept, independent of hardware
TCP/IP runs on all sorts of media
• Ethernet wire
• Wireless (many flavors: 802.11 wi-fi, Bluetooth, cable internet, StarLink, etc.)
• Fiber Optic
• Etc…
It can do this because it is layered--the higher levels hide the type of wire used

## Slide 4: TCP/IP Protocol Stack
Link
Internet
Transport: UDP
Transport: TCP
Application
Hardware: ethernet,
radio, fiber optic, etc.
Internet Routing
Sockets
DoD M&S Network
Protocols & lots more
Protocol
Protocol

## Slide 5: Layering
TCP/IP Sockets
Ad-Hoc
Protocols
DIS
HLA
Web
Application/Simulation
Application layer is above transport, link layers

## Slide 6: Layering
Notice that hardware (link layer) is isolated from application at the top. This means you can swap out the link layer every few years as faster media becomes available, and not affect your application at the top.
Understanding this is a Big Deal. The vast majority of money, design and programming time are tied up in application layer, and you can’t throw that away every few years.
Things like web browsers or games are written in such a way that they are completely isolated from hardware transport.
This allows us to create standards at the application layer that are stable over a period of decades.

## Slide 7: TCP/IP
TCP/IP gives you the ability to send some bytes from one machine to another. As far as TCP/IP (below the application layer) is concerned, it’s all just bytes. TCP/IP doesn’t try to interpret what the bytes are; that’s done at the application layer.
The application layer “makes sense” of those bytes, according to the pre-arranged application protocol — what data is being sent with what semantics (and often, when the data is exchanged).
Application layer is where we standardize M&S network protocols. Note that the “application layer” includes both
simulation data-exchange protocol (DIS, HLA, etc.) along with
what we think of as the distributed application (OneSAF, etc.).
Notes: Data format = syntax, dats-structure meaning = semantics

## Slide 8: Application Layer
This is where DoD M&S network standards live. There have been several over the years:
• Ad hoc: Created as needed for proprietary or unique systems; elder days to present
• Distributed Interactive Simulation (DIS): 1993 to present
• High Level Architecture (HLA): circa 1998 to present
• TENA: circa 2000 to present
• Emerging XML/JavaScript/JSON standards: not actually broadly adopted standards per se, rather variations of data encoding.
Protocols are usually embedded in applications like OneSAF, Janus, etc. “Application layer” in network-speak usually refers to the protocol-connections layer, not the whole application.

## Slide 9: Ad Hoc Protocols
In the early years people just went out and did stuff, because it was all new…
This meant that the Boeing simulator didn’t talk to the LockMart simulator, and furthermore the LockMart aircraft simulator might not talk to the other LockMart aircraft simulator…
Protocols were all typically built on top of Unix sockets (UDP and TCP)
But it worked, sort of… but not interoperable, typically.
This approach still common in commercial games industry.
Why? What relevance does this question have to DoD?
Notes: LockMart = Lockheed Martin

## Slide 10: Distributed Interactive Simulation (DIS)
Widespread lack of protocol standards led to DIS. Everyone in procurement realized that lack of interoperability was bad, so they got together and agreed upon a standard for M&S.
Agreed upon by SISO, ratified as IEEE standard.
This means anyone can read the standard, implement it, and have their simulator be interoperable with another DIS simulator.

## Slide 11: High Level Architecture (HLA)
HLA is a follow-on design to DIS, intended to address a wider range of simulations and abstract away some of the network details.
DIS was “first person shooter” oriented, while HLA can be used in wider range of simulations, such as time-step controlled.
HLA enables object models, hides socket layer, handles things like shared timing, but pushes
data semantics to application designers, and
data protocols to independent frameworks.
Notes: C2SIM
- Protocols for both: syntax and symantics
Bridge LVC MES with C2
SISO and NATO

## Slide 12: TENA
Test & Training Enabling Architecture (TENA)
used in test ranges, both in US and abroad.
Design similar to CORBA, the Common Object Resource Broker Architecture.
CORBA is a distributed object technology, widely standardized since the 90’s.
There is considerable overlap between three major approaches: DIS, HLA, and TENA.

## Slide 13: Emerging XML and JSON
The field occasionally looks at new approaches to definitions, encodings of data exchange based on XML and JavaScript/JSON syntax.
See for example WebLVC, which integrates many DIS/HLA concepts but uses JSON as a “wire format” for data units themselves.
Key merit: well-defined data exchange (meaning semantics) into (and out of) any Web browser. Note: no executable code.
Notes: Parsing of data structures
Validation! Is the data ok? Avoids „Garbage In Garbage Out“

## Slide 14: Communications
TCP/IP is the basic networking framework for communicating information between devices.
“Devices” is a broad term. Can include user desktops, cell phones, Internet of Things (IoT), toasters and coke machines, hybrid embedded systems, diverse robots, etc.

## Slide 15: TCP/IP Role in Network Layers
Link
Internet Protocol
Transport: UDP
Transport: TCP
Application
Hardware: ethernet,
radio, fiber optic,
i.e. physical layer
Internet Routing
Sockets
DoD M&S Network
Protocols + lots more
review

## Slide 16: Link Layer
Link layer: this is the hardware layer (e.g., ethernet, 802.11b)
The network switch you can get at Best Buy is an example of a link layer device.
Just add physical layer: Cat5 Ethernet cable, wireless, fiber-optic cable,
DirectTV, Starlink, etc.

## Slide 17: Link Layer
You can easily spend an entire semester studying only the link layer.
You use it and see its effects every day.
We will assume it magically/effectively works…

## Slide 18: Internet Protocol (IP) Layer
The next layer up is responsible for routing packets to their intended destination, via whatever path is required.
When you send “War & Peace”, TCP/IP breaks up the text into packets, routes the packets to the destination, and then reassembles them back into the original text.
The IP layer is responsible for getting the individual packets to their destination process.
Routers handle IP. Examples include Barracuda, Cisco, Dell, D-Link, NetGear, Qualcomm, et al. These are (often) expensive and may require major geek support to run.
IP is mostly opaque to application programmers.
We will assume it all magically works, which (based on everyday experience) is usually a good assumption.
Notes: https://www.bing.com/search?q=router+companies

## Slide 19: Transport Layer
Transport is the “sockets” layer. These APIs are where the developers of application layers mostly do work.
Sockets are a way to send bytes from one device to another (or from the same device to itself).
Sockets don’t know anything about the content of the messages being sent--to them it’s all just a bunch of bytes. IOW, it’s a way to present a byte array to a program and say “here, you make sense of this...”
… the program then interprets the bytes and does something with them (extracts state data, in our case).

## Slide 20: Layers
Link
Internet
Transport: UDP
Transport: TCP
Application
review

## Slide 21: Socket Types: TCP, UDP
Notice that in transport layer supports two types of sockets: TCP and UDP. These are intended to handle two different application uses
You can use either or both in single application.
I.e. OneSAF can use both a network protocol based on TCP and another one based on UDP, all at the same time.

## Slide 22: TCP Sockets
TCP sockets have some important properties:
• Reliable delivery of data,
• In-order delivery of data to application,
• No duplicates of data packets,
• Built-in rate control, adjusts to network capacity.
What this combination attempts to replicate is:
reading and writing a stream of data to a file.
Notes: “a stream is a stream is a stream” meaning an ordered and reliable sequence bits/bytes

## Slide 23: TCP Sockets Guarantee
Reliable: if you send data, there won’t be random dropouts in data sent (that you see).
Recall that TCP/IP breaks up big chunks of data into many packets to send across the network.
“Reliability” means that if the network somehow drops one of those packets, it will be resent and resynchronized with originals (if needed).
Or else… it fails, and reports problem as such.

## Slide 24: TCP Socket Characteristics
In order: When TCP/IP breaks up all the packets for sending, it will ensure that the packets are re-assembled in the same order they were sent to the receiving side.
No duplicates: in some obscure situations, the underlying network may duplicate packets. TCP ensures that the duplicate packets are discarded (rather than getting redelivered).

## Slide 25: TCP Sockets: Rate Limiting
Rate limiting: What if you have a really fast server computer sending to an iPhone? The server has a really fast CPU and is hooked up to a fast network; often it doesn’t necessarily know whether it is sending to a slow CPU across a slow network
Without a rate-limiting feature you can easily overwhelm the receiving machine and network – effectively it’s a sort of like denial of service attack.
TCP automatically throttles back the sending rate if too many packets are being dropped (and slowly recover)
Notes: .

## Slide 26: TCP
TCP Socket
TCP sockets replicate writing to a file; data is sent
(and received) across a full-duplex connection
Writing to a file: open the file, write data, close the file.
Data appears in file: reliable, in order, no dupes, rate limited.
Same with TCP sockets – a stream is a stream is a stream.
Host A
data
Host B
data

## Slide 27: UDP Sockets
UDP is interesting alternative to TCP sockets that eliminates some of the features of TCP.
• Unreliable data delivery--there is no guarantee that the receiving application will get everything you send,
• Data may arrive out of order, without re-assembly back to the original order
• Duplicate data may arrive via different routes,
• There is no built-in rate limiting,
• Packet-oriented rather than stream-oriented.
Notes: A stream is a sequence of packets (i.e. an ordered array of bytes)

## Slide 28: UDP Sockets
Some of these “features” seem counter-intuitive. Why on earth would you use an API that may throw away data?
The issue is that TCP introduces some overhead in latency and (to a lesser extent) bandwidth.
Sometimes we have applications that work well if most of the data is received.
Example: position updates in a game or exercise.

## Slide 29: UDP Sockets
“The player on my computer
is controlling a tank, and I will send out updates of its position every 1/30th of a second”
What happens if one out of a hundred updates is dropped?
What happens if 99 out of a hundred updates is dropped?

## Slide 30: UDP Sockets
UDP is packet-oriented rather than stream-oriented.
In UDP you create discrete messages and send them.
TCP is handled much like reading and writing from a file, which is just a long stream of bytes.
A stream is a stream is a stream…

## Slide 31: Sockets – common purpose
Note that both TCP and UDP sockets are responsible only for sending data. They do not attempt to make any sense of the data itself--that is the responsibility of the next layer up.
Similarly, files are not responsible for format or meaning of data written to them--that’s the responsibility of applications that read or write the file.
The sockets API only gets data to the destination; once there, the application has to make sense of the data.

## Slide 32: IP version 4 Numbers
Every host (computer) on a network is assigned a unique IP number, usually written like this:
192.168.1.10
This is called the “dotted decimal” format. In reality the IP is 4 bytes long, and each number can (sort of) be in the range of 0-255.
This uniquely identifies the computer on the network; you can’t talk to something directly unless you have a name to distinguish it, and the IP is the “real” name of the computer in TCP/IP
“I want to connect to the host 131.120.7.15” will connect you to a particular host on the internet

## Slide 33: IP Numbers
You can see what IP your computer has by going to Control Panel->Network->TCP/IP->Properties, or “ipconfig /all”, or on OS X Control Panel->Network, or on Linux “/sbin/ifconfig”
How are IPs assigned? If we have unique numbers for hosts, then we have to have some way to ensure that each host is configured with a unique IP number
Two basic ways:
• Manually configure
• Dynamic Host Configuration Protocol (DHCP)

## Slide 34: IP Numbers
Manually: go to each machine, type in the IP number
What’s wrong with this? …discussion…
DHCP: when the host boots, it contacts a server and asks for an IP. The server assigns an IP to the host from a floating pool of available IP numbers
The host has a “lease” on the IP number for a limited time. After the time is expired, the server takes back the IP (unless the lease has been renewed).
Why this approach? Why not have the computer “resign” or “reassign” the IP when done?

## Slide 35: Dynamic IP addresses
DHCP has a “weakness” in that a host may be assigned a different number the next time it boots.
This is perfectly OK for desktop clients, but not for servers. Typically, people want to contact servers, and if the server IP number is constantly changing, then they don’t know how to address and reach it. Clients, on the other hand, spend their time contacting servers and not often being contacted.
For example:
• Manually assign IPs to servers
• Have laptops & desktop clients use DHCP

## Slide 36: Domain Name Service (DNS)
Suppose you want to connect to a web server. It would be bad to force users to memorize “72.21.210.11” rather than “amazon.com”
DNS maps a name to an IP number. This is done by a server sitting on the network. Your host contacts the DNS server and asks “what is the IP for www.nps.edu?” The DNS server responds with the IP.
The DNS server to reach is set on your host by DHCP (usually), can also have a fixed value.
Notes: $ tracert amazon.com
Tracing route to amazon.com [54.239.28.85]
over a maximum of 30 hops:
1 3 ms 4 ms 4 ms 172.20.144.1
2 3 ms 3 ms 2 ms pa-v400.ern.nps.edu [172.20.0.7]
3 3 ms 2 ms 2 ms 205.155.65.225
4 5 ms 9 ms 5 ms dc-svl-agg4--nps-100g.cenic.net [137.164.24.188]
5 5 ms 6 ms 5 ms 151.148.9.206
6 * * * Request timed out.
7 * * * Request timed out.
8 * * * Request timed out.
9 * * * Request timed out.
10 * * * Request timed out.
11 * * * Request timed out.
12 * * * Request timed out.
13 * * * Request timed out.
14 69 ms 66 ms 66 ms 54.239.28.85
Trace complete.

## Slide 37: DNS
DNS Server
“give me the IP for
www.nps.edu”
“the IP is 172.20.20.11”
name | IP #
www.nps.edu | 172.20.20.11
Beatnik.ern.nps.edu | 172.20.18.4
Mail.nps.edu | 205.155.4.2
The DNS server maintains a table matching names to IPs
Notes: $ nslookup www.nps.edu
Server: dc01-srvdcp.ern.nps.edu
Address: 172.20.20.11
Non-authoritative answer:
Name: www.nps.edu
Addresses: 52.42.202.22
52.36.234.65

## Slide 38: DNS
The campus admins can enter the IPs for all the server hosts on campus. But what if we want to use a name to refer to a server off campus, like amazon.com?
The campus admins have no idea what assignments Amazon is making, and what’s more the DNS server can’t realistically have a database with every host name on the internet.
To refer to a host name off campus, the local DNS server simply asks Amazon’s DNS server to resolve the name on our behalf

## Slide 39: Off-Site DNS
“give me the IP for
Amazon.com”
“the IP is 72.21.210.11”
Campus
DNS Server
Amazon.com
DNS Server

## Slide 40: DNS
The campus DNS server contacts amazon on your behalf, gets the IP number, returns it to you, and caches the result for some period of time so later lookups are faster
Potential problems?
>nslookup www.apple.com
Non-authoritative answer:
Name: apple.com
Address: 17.149.160.49
The “non-authoritative” means the local DNS server got it from cache

## Slide 41: DNS
So how does the local DNS server know how to contact the Amazon DNS server?
When a domain like nps.edu or amazon.com is registered, one of the required pieces of information is at least two DNS servers
You can see the same information using whois protocol:
http://www.networksolutions.com, “whois” link

## Slide 42: whois
Registrant: contact info
Admin Contact: the suits
Technical contact: the t-shirts
DNS Servers: the names of the servers where the name-to-IP information is entered
You can set up your own DNS servers or use someone else’s as a paid or free service
This is the standardized way for the info to get into the system

## Slide 43: DNS
The internet maintains 13 “root DNS servers”. These server IPs are hard-coded into a local DNS server’s config file
In reality it is a lot more than 13 servers; each are really clusters that are geographically distributed
These root servers use the data entered during the domain registration process to direct a DNS server that has the information needed

## Slide 44: Root DNS
Root
Edu
Com
Org
Net
XXX
Uk
Amazon
Apple

## Slide 45: DNS
When your local DNS server starts up cold, it has the root DNS servers. The first time it gets a request for amazon.com, it goes there, gets the .com DNS server, and then asks the .com server for amazon’s server.
All these answers are cached, so after the Top-level Domains (TLDs) are retrieved it doesn’t need to talk to the root servers.

## Slide 46: DNS
The net result: you can refer to a host by name rather than IP, and as long as you have a functioning DNS server it will all work.
Meets the long-term success metric: “easy!”

## Slide 47: DNS & Info Operations
Obvious question: what happens if the DNS server (either locally or TLD or root) is compromised?
For example, a citizen in country under attack decides to bring up the local newspaper site; instead they are redirected to the attacker’s propaganda site.
This is used as part of the “great firewall of China”. PRC uses DNS servers (for example) to redirect facebook.com to alternative servers.

## Slide 48: Stupid DNS Tricks
DNS can be used to aid scalability
• Round-robin DNS: The DNS server returns a list of IP numbers rather than a single IP, and the client just picks one. All the servers have identical content.
Now you have N servers to handle the load in a balanced fashion, instead of just one.

## Slide 49: Stupid DNS Tricks
Geographically based DNS: There are lists of IP numbers and their approximate location. Based on the IP of the client making the request you can return an IP that’s close to the client.
In Europe if you go to google.com you’ll get the language and country-specific site that reflects the IP of your computer.

## Slide 50: Content Distribution Network (CDN)
The idea of a CDN is to put the content close to the client. This is important for broken things like NMCI.
This is done by playing DNS tricks—as with geographic DNS, the request is sent to a server “close” to the client with a full copy of the site content. If the content is not present at the CDN, it’s pulled down from the authoritative server.
Vendors: Akamai, Google, AWS, many others

## Slide 51: Port Numbers
Suppose you have a server named “nps.edu” that runs mail and a web server. You want to contact it, so you refer to it by IP number (perhaps after a DNS lookup).
But which program on the host do you talk to? The server is running both mail and web…
We need some further way to specify which service on the host we want to talk to: mail, Web, DNS, OneSAF, YourThesisSimulation, etc.

## Slide 52: Port Numbers
Each host (IP number) has ports that range in number from 0-64K. There is a separate port range for TCP and UDP, they are not the same
  so UDP port 25 is not the same as TCP port 25
By convention, certain programs listen on certain ports. For example, mail servers traditionally listen on TCP port 25, and web servers on TCP port 80.
So: to contact a web server at www.nps.edu, you should refer to IP 205.155.7.12 and port 80. If a mail server is also running, you can contact it at 205.155.7.12 and port 25.

## Slide 53: Port Numbers
How do you decide what port number goes with what service? All participants need prior knowledge of this
The IANA/ICANN maintains databases of various arbitrary number assignments for the internet
http://www.iana.org/assignments/port-numbers

## Slide 54: Summary
TCP/IP layering
UDP and TCP sockets
IP numbers
DNS
Ports