## Slide 1: User Datagram Protocol (UDP)
Don McGregor
Don Brutzman
MOVES Institute
brutzman@nps.edu

## Slide 2: UDP vs TCP
UDP and TCP are both part of ... IP
TCP is good for sending reliable, in order, no duplicate flow controlled byte streams
But this has some costs that might not be immediately obvious
  Reliability may require retransmission
  Single Point to Single Point
UDP is an alternative… so is Broadcast…
All three are part of Internet Protocol (IP)

## Slide 3: UDP
What happens if the network drops some data being sent in TCP?
The receipt of data on the other application stops until a time-out expires and the data is resent and received
If we are sending continuous state updates, this means all data stops until the dropped data is resent and received
UDP is usually lower latency than TCP, and has less jitter
Latency and jitter are terms of art in networking.
  Latency refers to how long it takes a message to get from the source to the destination.
  Jitter is the standard deviation of latency

## Slide 4: TCP handicaps relative to UDP
What if we are sending position updates every 1/30th of a second (frame rate?)
  for example, a test range
If one TCP update gets dropped, another one is on the way. But due to the in-order delivery requirement, we can’t provide new state updates until sender goes through a timeout/resend cycle
This means all delivery of state information stops until the now-outdated info is received

## Slide 5: Sequence Numbers
Is in-order delivery important for a protocol? Easy to include a monotonically increasing sequence number within your custom data.
  (i.e. not worrying at all about TCP sequencing)
If you then get a sequence number equal to or before the last-received sequence number, you might (optionally) throw a packet away. That indicates the data is old, or arrived out of sequence.
Thus including sequence numbers or full-fledged timestamps (or both) provides good value

## Slide 6: Stream versus Packets
TCP sockets are stream-oriented. You read or sent a stream of bytes, like reading or writing from a file. (InputStream, OutputStream)
TCP uses character markers in the stream to delineate messages, called “framing”. In TCP we usually used newline characters to delineate the boundaries between messages, but you could in theory also use byte counts.
UDP is packet-oriented. You compose discrete packets or messages, then send them. (An array of bytes, usually)
UDP is analogous to sending postcards (did that arrive?)
UDP packets can be big (up to 64K), but you should keep them below MTU of 1500 bytes, better 512 bytes, for performance reasons. This is usually easy to do.
  Above MTU means a message has to be split (and recombined)

## Slide 7: Message Contents
In TCP it was best to use (or start with the assumption of using) text, because it was universal and easy to debug. But with numeric data we often use binary
  Text is larger than binary. Examples are numerous/unavoidable.
  Double precision floating point = 64 bits binary
  Plain-text double = 16 digits (8 bits/char) = 128 bits, bigger
In UDP we are often dealing with data that is low latency and numeric. Position updates, streaming audio, streaming video, etc.
It usually makes sense to use binary data for this, but this choice introduces all sorts of potential problems…

## Slide 8: Message Contents
Binary float and double value formats vary from CPU to CPU and operating system to operating system – ouch! Difficult, picky…
The good news is that what bits make up a shared “float” or “double” value is uniformly standardized by IEEE.
However the bad news is that byte order is not. Different CPUs may arrange the bits and bytes within a float in different ways…
This potential interoperability issue is solved by “network byte order”

## Slide 9: Byte Order and Endian
From least to most significant bit (integers)
1 2 3 4
The same number may be represented as
4 3 2 1
in a different CPU. Same value, different bits.
This characteristic of bit formats is called “endian”, as in big endian or little endian, a hangover from the elder days of computing.
https://en.wikipedia.org/wiki/Endianness

## Slide 10: Byte Order
Luckily, in Java these issues are taken care of for you so long as you stick to the standard input and output streams on both sides.
If you work with C or other lower-level languages, this is not necessarily taken care of for you, and your programs need to be alert to the implications.
But as long as it’s Java on both ends, you will be OK, and even if it’s not Java it may work (by accident?!)
Internally, Intel CPUs use the opposite of the “standard” network byte order – go figure. Not sharable.
BIG-endian byte order also known as network byte order.

## Slide 11: Protocols
How should we arrange the data? With text, we could simply put it in some easily parsed text format that we could also read.
With binary, we need prior knowledge of how the data is laid out, so we can read it correctly. If the data isn’t read in the same format as it was written, you’ll interpret received data as garbage
GIGO: Garbage In Garbage Out
Note: also want a recovery plan if error(s) occur!

## Slide 12: Java Binary Data (in memory)
ByteArrayOutputStream baos = new ByteArrayOutputStream();
DataOutputStream dos = new DataOutputStream(baos);
dos.writeFloat(17.0f);
dos.writeFloat(23.0f);
byte[] buffer = Baos.toByteArray();

## Slide 13: Java Binary Data
The data is now in an array of bytes. This is cross-platform, as long as the receiving side knows the byte order
Floating Point Value 1
Floating Point Value 2

## Slide 14: Binary Data
Reading is straightforward
ByteArrayInputStream bais = new ByteArrayInputStream(buffer);
DataInputStream dis = new DataInputStream(bais);
float x = dis.readFloat();

## Slide 15: Reading Data
What happens if you read an integer from the data input stream instead of a float? A double instead of a float?
This means that you need prior knowledge of what format the data is in so you don’t get garbage out
  So you really need to know the protocol
It is a very good idea to have a protocol version number in the first slot of the binary data
  Allowing future extensibility and protocol changes
Usually a good idea to have a sequence number as well (which is much easier to handle than a timestamp value)

## Slide 16: UDP Sockets
You create UDP (or “datagram”) sockets in one line. These are unconnected. With TCP, we had a stream connection to another host. With UDP it’s like an open mailbox that anyone can drop messages into
DatagramSocket socket = new DatagramSocket(4545);
Note no other IP, just the UDP port number (which is distinct from TCP port number)

## Slide 17: Datagram Packets
The discrete messages being created are DatagramPackets. These contain an address (the port and IP of the machine they are being sent to) and a payload.
The payload is our binary data
  byte[] buffer; …// fill in buffer contents here
  DatagramPacket packet = new DatagramPacket
  (buffer, buffer.length, ipAddress, port)
  socket.send(packet);

## Slide 18: UDP vs TCP (repeating, important)
UDP is packet-oriented, TCP is stream-oriented
UDP is unreliable
UDP is not TCP! A common rookie mistake is to naively say “I want to use UDP, but I also want it to be reliable”….
Don’t do that. You will wind up creating a complex protocol that re-invents TCP, only much more poorly.
Understanding helps. Embrace the limitations of UDP 8)
There can be some situations where you add TCP-like capabilities to UDP, or complement UDP with a TCP channel, but you probably shouldn’t start off that way.
UDP + TCP in tandem together might answer the mail…
  Example: TCP for secure registration, then UDP for streaming

## Slide 19: Rate Limiting
TCP automatically throttles back the sender if it is overwhelming the receiver. Not so for UDP, it keeps going and going and going …
Due to nature of software, even if sender and receiver have same CPU speed, at full rate the sender can overwhelm the receiver.
Thus you must be careful that you don’t implement denial of service in your own software! Warning, this is default behavior unless you take steps to prevent it.

## Slide 20: Rate Limiting
Packets Sent/sec
Rec/sec
Packets received at high rates fall off a cliff
Nominal 100% is always
higher than the cliff itself…

## Slide 21: Data Loss: bad, or maybe good?
How to handle losses of position updates?
  Hmmm, is that necessarily a problem?
How about streaming audio data?
  One solution is to include redundant data (or hamming codes for error detection/correction) in multiple packets. If one packet gets lost you can recover the data from other packets
  Or… not. If you miss it, you deliberately miss it.

## Slide 22: Assignment
Write an application that sends, in binary format, an entity identifier and position
Include detailed annotated console showing
  Original data
  Comments/annotations