## Slide 1: Distributed Interactive Simulation (DIS) Protocol
Don Brutzman
Don McGregor
MOVES Institute
brutzman@nps.edu

## Slide 2: Standards are Valuable
In the UDP examples, we sent position updates, but these were only good for our own application.
What if we want to interoperate with other people and other applications?
We need to come to some sort of agreement on what the format of the binary messages will be.
This is what Distributed Interactive Simulation (DIS) provides -- a standard format for information like the kinds of things we sent in the UDP example

## Slide 3: DIS Design
DIS is designed to be peer-to-peer; no server needed. This drives many of the protocol design decisions, such as how to get unique entity IDs.
If you were designing DIS today you might consider relaxing this restriction. Server software was difficult and non-standard in 1990; web servers are trivially easy today.
As it turns out, DIS works well both with shared peer-to-peer and with client-server.

## Slide 4: DIS
DIS is simply a series of formats for packets (“Protocol Data Units” or “PDUs”) Each PDU contains a different sort of data: position, logistics, electronic warfare, etc.
Most commonly used is Entity State PDU (ESPDU).
Includes binary data for position, orientation, velocity, angular velocity, ID, what type of vehicle, and much more – in ESPDUs and in other PDU messages.
Very much oriented towards the military.
The exact position and format of every field is specified--the position of a field is so many bytes into the PDU, consists of three double-precision floating-point values, etc.

## Slide 5: DIS
A group of people got together at SISO, agreed upon the standard, refined it to meet many rules & requirements, and had it ratified as an IEEE standard. This took years, and still continues today.
Anyone can get the IEEE standard, read it, and implement it. The IEEE standard is the formal specification for the exact position and format of the fields.
With what you know now, you might even consider implementing parts of DIS yourself if you had to! Fortunately we can take advantage of this immense work.

## Slide 6: DIS
DIS actually specifies a few dozen types of messages. You can think of this as an object class hierarchy, or an implemented data dictionary with corresponding methods.
Different PDUs are used to describe different aspects of combat: position, shooting, logistics, electronic warfare, etc.
Every PDU message type starts with a header; this is the same for every PDU, though some field values are different.

## Slide 7: PDU Hierarchy
PDU
Entity
Info
Entity
State
Collision
Warfare
Fire
Detonation
PDU Family
PDU
Type
etc.

## Slide 8: PDU Header

## Slide 9: PDU Header
Protocol Version: release of DIS
Exercise ID: unique ID for each “battle” being fought, so two “battles” on the same network won’t interfere with each other
PDU Type: Fire, detonation, entity state, etc.
PDU Family: Entity Information, Warfare, etc
Timestamp: when the PDU was sent; also used for keeping track of duplicate packets and out-of-order packets
Length: byte length of PDU
PDU Status: bookkeeping and additional data
Padding: gets everything following word-aligned, space for further additions

## Slide 10: Enumerated Types
Note some things like the “PDU Type” are usefully described by numbers. For example, 1=Entity State PDU, 2=Fire PDU, 3=Detonation PDU, 4=Collision PDU
These “magic ” numbers are defined in the Enumeration and Bit-Encoded Values document (described later)
For now, just remember that these are arbitrary numbers, but they need to be consistent. We might just as easily reverse all these numbers, as long as everyone still agreed upon their meaning
If two simulations don’t agree on the enumerated values, we have interoperability problems
  What might cause the enumerated values to have a mismatch?
  Thus agreeing on enumerated values is a big part of solution…

## Slide 11: Entity State PDUs
We use ESPDU when want to inform other hosts of the position of an entity we control—the most common PDU
Entity sends ESPDU with
• Unique ID
• Position (xyz) in standard coordinate system
• Orientation
• What type of vehicle it is
• More….

## Slide 12: Entities
DIS is oriented towards controlling things in 3D. It is mostly, but not entirely intended to model vehicles and physical objects
A fundamental concept is entities, which represent one item: tank, plane, minefield, dismounted infantry, etc. Before we can say “hey you, move to (x,y,z)” we need some way to uniquely identify the thing to be moved so we can order it around
We need a unique identifier for each entity in the world; this is done with the EntityID, which consists of three values
  Site: on a multiple-location simulation (Norfolk, Monterey, San Diego) each site is assigned an ID
  Application: the identifier for one simulation application
  Entity: within one application, a unique identifier

## Slide 13: Entity ID
Example: before the simulation starts we agree on the following arbitrary numbers
Site | Number
China Lake | 42
Norfolk | 17
Orlando | 23
Application | Number
LockMart M1A2 Simulator | 112
Boeing UCAV Simulator | 417
JCATS | 512

## Slide 14: Entity ID
Tank
EID: (42, 112, 18) at (x0, y0, z0)
EID: (42, 112, 19) at (x1, y1, z1)
Boeing simulator at Norfolk
controls an aircraft
LockMart simulator at China Lake
controls two distinct tanks

## Slide 15: Entity ID
An tank entity controlled by the LockMart simulator at China Lake may have an entity ID of (42, 112, 17) and no other entity in the simulation should have the same entity ID
An UCAV entity controlled by a Boeing simulator at Norfolk would have an EID of (17, 417, 18), and no other entity should have the same ID
Note that this depends on all the participants agreeing to use the same arbitrary numbers! We’ll see the same phenomenon later with Entity Types.
This concept of Entity IDs is also used many places in HLA such as the RPR FOM and in some places in TENA

## Slide 16: Entity Type
We also want to know what type of entity is being described. This is done with the entity type record
The entity type record is a collection of numbers that together define what specific type of hardware this is, whether it’s air or land, and the country of origin
For example, an M1A2 tank from the US
Again, the meaning of the numbers is defined in the EBV document

## Slide 17: Entity Type

## Slide 18: Entity Type
{
Kind: 1 (entity)
Domain: 1 (Land)
Country: 225 (US)
Category: 1 (Tank)
Subcategory:1 (M1)
Specific: 6 (M1A2)
}
Whenever a DIS message has a record with the above settings we know
it’s referring to an M1A2 tank

## Slide 19: Enumerations
We want a compact and unambiguous way to express something like “M1A2 tank from the US with mine rollers”, so each of these fields is represented with a number, called an enumeration.
The SISO standard has an agreed-upon listing of the values for this. When the kind is Platform (1), domain is land (2) country is US (225), and the category is 1, subcategory is 1, and extra is 3, it represents a US M1A2 tank
If you receive a PDU that contains an entity type of the above, you can use this information to correctly draw the tank

## Slide 20: Enumerations
Note that this depends on everyone being consistent with respect to the EBV document! There was some drift on this over the years, and this is a management/technical problem that is now solved by SISo.
Prior example. Suppose some application from 1995 uses an enumeration for Yugoslavia, the app was never updated, and that enumerated value is now used to describe East Timor in more recent EBV documents
The more recent apps using the current EBV will see the entity as East Timorian, and old applications will see it as Yugoslavian.

## Slide 21: EBV Document

## Slide 22: Entity State PDU
The most commonly used PDU is the Entity State PDU. This represents the state of one entity at one point in time.
Includes fields for position, orientation, velocity, acceleration, angular velocity, etc.
Also includes an enumeration representing type of dead reckoning algorithm to use.
These are sent out by every entity every few seconds.

## Slide 23: Entity State PDU (Partial)

## Slide 24: Fields (in PDU Header)
Timestamp: remember how UDP does not ensure in-order delivery or no duplicates?
The timestamp field is used to work around this. An application can throw away a PDU if the timestamp is less than or equal to the timestamp of a packet already received.
This means you may see not see an effect of your packets if you fail to set this; timestamp that is always zero means the receiving application may consider the packet a duplicate and discard it.
Synchronizing clock time among participants is important.

## Slide 25: ESPDU Fields
EntityID: Unique identifier for the entity whose state is being updated.
ForceID: what if we have three or four sides to the battle: red, blue, white, etc.
EntityType: combination of values that tell you the type of vehicle being updated.
AltEntityType: some vehicles may be able to represent themselves as something else, such as an US F-16 aircraft using ECM to appear to be a Yugoslavian Mig-29. AltEntityType is what the vehicle appears to be to forces other than its own.

## Slide 26: ESPDU Fields, continued
Location: location of entity in 3D world. This creates an interesting problem because we need a common coordinate system. What should we use?
DIS is intended for all sorts of diverse uses, including space and underwater applications, so lat/lon/altitude is not always the best.
DIS choose an earth-centered Cartesian coordinate system… not very intuitive.

## Slide 27: Location

## Slide 28: Defining Location
This turns out to be a mixed bag; if you want to move a vehicle 100m east on the surface of the earth, it’s not immediately apparent what coordinates change, and in fact different coordinates will change depending on where you are on the earth. OTOH you can represent lots of types of movement
There are libraries from SEDRIS that do the conversions, though.
Some people cheat and simply use lat/lon/altitude or a local coordinate system of their own devising. This makes things completely incompatible with everyone else

## Slide 29: Global Coordinate Systems

## Slide 30: Placing a Local Coordinate System

## Slide 31: Local Coordinate System
DIS ESPDUs on the wire always use ECEF/Geocentric/World
Coordinates/earth centered, but when doing simulations we almost
always like to use scene coordinates. So convert from scene
coordinates to world coordinates when sending the DIS update

## Slide 32: Local CS
Everybody who does a simulation in 3D wants to use their own coordinate system, and has different conventions for which way which coordinate axes point. Everybody argues about the “right way”; this means you have to be prepared to handle almost anything.
Y North, X east, and Z up is used by some
It’s handy to have a local flat rectilinear CS when working with vehicles over a few KM

## Slide 33: Local Coordinate Systems

## Slide 34: Coordinate Systems
The diagram illustrates some of the problems: the earth is curved but we generally like to flat rectilinear coordinate systems. This sets up two local coordinate systems that overlap. We can convert point locations between CS’s, perhaps with some slop
Flat-to-spherical error is about 3m over 20KM, but modern warfare can operate in larger areas (artillery range 30+KM)
Aircraft like to have a local, body-centric CS, with x through the front, y out the right, and z down. This is used with Roll, Pitch, Yaw. These are often labeled (u,v,w)

## Slide 35: Aircraft Coordinate Systems

## Slide 36: Orientation
DIS describes orientation of an object via rotations around the DIS global coordinate system axes of X, Y, and Z
Rotate specified amount around X axis;
Rotate specified amount around original Y axis;
Rotate specified around around original Z axis

## Slide 37: Earth Models
To make things worse, the earth is not perfectly round. The WGS84 geoid describes an ellipsoid shape.
We may also have terrain on the ellipsoid (perhaps described by DTED data), air vehicles may be at some altitude, subs may be underwater, etc

## Slide 38: Head Explode
Do the math to convert an angular acceleration at Lat 38.123, Lon -118.56, at 500m elevation to global coordinate system
Do the math to convert +5 deg pitch on an aircraft in a local coordinate system to that of another local coordinate system
The good news is that this can be done with sufficient trig, and that you don’t have to derive it

## Slide 39: Location
The SEDRIS SRM libraries do the fancy math necessary to convert between coordinate systems
Convert from (lat, lon, alt) to geocentric DIS coordinates
From DIS coordinates to (lat, lon, alt)
Orientations: roll, pitch, yaw to “Euler angles” in the DIS coordinate system
Convert a distance offset to the new DIS coordinates
Create a local flat, Euclidian range coordinate system
Body-centric coordinate systems
http://www.sedris.org/hdr1trpl.htm

## Slide 40: ESPDU Fields
Linear Velocity: vector with entity linear velocity
Entity orientation: which way it is pointing. Euler angles in the entity’s coordinate system; rotations about x, y, z axis
Entity appearance: a series of bit flags that tell you about how to draw the vehicle. Camo? Smoking? Burning? Etc.

## Slide 41: ESPDU Fields
Dead Reckoning is a way to make a best guess about the entity position and orientation in the absence of updates. You can use all sorts of algorithms for this: velocity, acceleration, angular velocity, etc.
The DR algorithm enumeration tells you what technique to use, and the entity’s linear acceleration and angular velocity are included
You can also include DR parameters for other DR algorithms

## Slide 42: ESPDU Fields
Entity Marking: Up to 10 characters that can be used for things like drawing numbers on COMBLOC tanks, debugging info, etc.
Capabilities: bit flags that define things like its ability to supply ammo, fuel, etc. Mostly unused
Variable Parameters: a list (the length of which is defined earlier) that describes things like attached or articulated parts: the turret on a tank, gun elevation, etc.

## Slide 43: Articulated Parts

## Slide 44: DIS Mechanics
Suppose we have a simulated tank being controlled from one host. Periodically it will send out updates to the other hosts participating in the simulation
All hosts maintain a database of entities they know about. The receiving host uses the update to modify the position & orientation of the entity, and optionally redraw the entity on the screen
One host has definitive knowledge about the entity. Other hosts may have time-lagged information about the entity

## Slide 45: DIS Updates
Tank 1
Host 1
Host 2
Tank 1
Tank 2
Update
Tank 2
Update

## Slide 46: DIS Updates
Suppose two hosts are in an exercise, and later a third host joins. How does the new host learn about all the entities in the world?
What are some possible algorithms?

## Slide 47: DIS Heartbeat
DIS uses a heartbeat strategy: entities will periodically send out ESPDUs even if they have not moved or changed state. This allows everyone in the simulation to learn of other entities within one or two heartbeat cycles
Usually set to 5-10 sec. Stationary entities, such as minefields, may be longer (60 sec)

## Slide 48: ESPDUs
With just the ESPDU, what do we have?
We can
  Show entities moving in a 3D world
  Correctly map the right 3D model to the entity
  Gain knowledge of all the entities in the world
  Do dead reckoning
  Handle things like smoking, on fire entities
  Draw text associated with an entity

## Slide 49: Fire PDU
Since we’re the military, we also want to shoot at stuff. This is handled with the Fire and Detonation PDUs
The Fire PDU contains
  Who’s shooting (EntityID)
  EntityID of target
  Launch location
  Fire rate, etc
  Velocity
  Range
  Some other stuff
We may create an entity that represents the ammo in flight, as with a missile. Receivers of the fire PDU can draw the effects of shooting

## Slide 50: Detonation PDU
The Detonation PDU represents the impact of a munition, or other events such as a mine blowing up
  Target, shooter IDs
  Fuze type (from EBV document), velocity, etc
  Location
  Detonation result

## Slide 51: Detonation
DIS is cooperative in that it assumes no one is trying to spoof the system, issue fraudulent PDUs, ignore damage results, and so on
This is a bad assumption in commercial games, and one reason commercial games are often client/server rather than P2P. The server can issue more trusted assessments of damage

## Slide 52: DIS APIs
We need to put the information contained in the PDUs onto the network in a very specific format. How do we do that?
The bad way: every time you write a simulation write your own code
The better way: write a series of classes that let you work with the update messages as objects, then automatically put them into DIS format to send. Also code to convert the DIS format to objects.

## Slide 53: Open-DIS
PDU Information
In IEEE
Format
PDU Information
In Java
Format
PDU Information
In XML
Format

## Slide 54: Open-DIS
The idea is that you can convert the binary wire information into an object, and convert the Java object into an XML or JSON representation
The information is the same; we’re just keeping it in four different formats, and converting between them
There are also programming language objects for C++, C#, and Objective-C (iPhone, OS X), Python, Javascript

## Slide 55: Open-DIS
On the wire you’d almost always want to use IEEE format, simply because that’s a standard
It’s useful to have the information in a Java object for manipulation and calculations
XML can be useful for archiving and web services
You can also use Java object serialization format (utterly non-standard), JSON, XML, etc

## Slide 56: Open-DIS
The Open-DIS project has implemented classes for the several dozen PDUs. Each PDU has code to marshal itself to IEEE DIS format, and read from DIS format.
https://github.com/open-dis
For Java, include open-dis.jar in your project, along with supporting jars
Language implementations for C++, Javascript, C#, etc.

## Slide 57: Open-DIS (Java)
EntityStatePdu espdu = new EntityStatePdu(); espdu.setTimestamp(timestamp); Vector3Double position = espdu.getEntityLocation();
position.setY(0.0); position.setZ(0.0);
ByteArrayOutputStream baos = new ByteArrayOutputStream(); DataOutputStream dos = new DataOutputStream(baos); espdu.marshal(dos);
byte[] buffer = baos.toByteArray();

## Slide 58: Open-DIS (Java)
Decoding is straightforward
PduFactory pduFactory = new PduFactory();
Pdu pdu = (Pdu)pduFactory.createPdu(packet.getData());
Pass the factory object an array of bytes in DIS format. You get back an object of the correct PDU

## Slide 59: Open-DIS (Javascript)
// How to create dis binary messages
var espdu = new dis.EntityStatePdu();
espdu.entityID.site = 17;
var dataBuffer = new ArrayBuffer(1000);
var outputstream = new dis.OutputStream(dataBuffer);
espdu.encodeToBinaryDIS(outputStream);
var trimmedData = dataBuffer.slice(0,outputStream.currentPosition);
// How to decode binary dis messages
var pduFactory = new dis.PduFactory();
var disMessage = pduFactory.createPdu(binaryData);

## Slide 60: Other PDUs
Most of the PDU traffic is ESPDUs. Something like 90+% of PDUs in an exercise are ESPDUs
Also PDUs for logistics, electronic warfare, etc

## Slide 61: Example
DISMap at github, https://github.com/mcgredonps/DIS_Map
This uses Java (on the server side) and Javascript (on the web page, on the client side)
The Javascript in the web page sends DIS to the server, which is written in Java

## Slide 62: DISMap
Web Server
Network with
conventional
binary DIS
Web pages with Javascript
WebGL scene updated by
DIS over a Websocket

## Slide 63: X3D
EspduTransform {
address "239.1.2.3” port 62040
siteID 0 applicationID 1 entityID 0
networkMode "networkReader"
children
[Shape { appearance Appearance { material Material
{ diffuseColor 1 1 0 }} geometry Box {size 1 3 9} }
]
}

## Slide 64: Wireshark
Wireshark has a built-in decoder for DIS
• Analyze->Enabled Protocols to make sure DIS is turned on
• Select a packet
• Analyze->Decode As to view as DIS; can also set all packets sent to or from a port to be automatically decoded as DIS

## Slide 65: Wireshark Capture

## Slide 66: Big Picture
Notice that we have a lot of semantics that go along with the protocol
  A coordinate system
  Dead reckoning algorithms
  Enumerations that define things like vehicles
  Assorted visual cues (appearance)
  Define some operations like shooting at people
  Assumptions about munitions
All this is very difficult to create from scratch; we will see these reused in HLA and TENA

## Slide 67: DIS
Notice that we are relying on trust, and not expecting the users to do things like spoof packets, write bots, incorrectly assess damage when shot at, no replay attacks, and so on
This is a very bad assumption in the commercial world, not so bad of an assumption in the military world
Encryption of packets is fairly cheap computationally which can cut down on some of these griefing issues

## Slide 68: Semantics
Doing something as seemingly simple as moving objects around in 3D has become very complex because we have to agree on so much about what the data means. Units, coordinate systems, enumerated values, order for exchanging packets, time systems, dead reckoning algorithms, byte order….
Think about how complex agreeing on higher order semantics like mission orders in C4I is

## Slide 69: Project Ideas
Given the Entity Type, load a correct 3D representation
PDU recording and playback of exercises
Hook up your graphics class project to DIS