## Slide 1: Network Scalability
Don Brutzman
Don McGregor
MOVES Institute
brutzman@nps.edu

## Slide 2: Scalablility & Bandwidth
Suppose we have one host sending out updates of its position
Assume that there are five different hosts that also want to share this information.
How do we deal with this?
  Once you figure that out, how about 50? 500? 5000? More?

## Slide 3: Scalability
Option 1: send out the same data five times
Bad; this means we use 5X the bandwidth and it takes 5X as much time to send. What happens if we have 1000 other hosts? What if each of those is also sending updates?
The data sent by a single host scales linearly with the number of hosts; the total data on the network scales with the square of the number of participants
This is a recipe for (eventual) disaster

## Slide 4: Broadcast
Broadcast works only within one network. It uses a special IP number with host portion set to all 1’s.
e.g. (example given), 172.20.81.255
This only works with UDP (why? reserved address)
One copy of the data goes onto the network. Everyone who is listening receives it – because that is a requirement of broadcast protocol itself
  i.e. a hardware requirement
Example: sound powered phones, positive repeatback is part of the protocol for use
(Netmask defines “host” and “network” portions)

## Slide 5: Broadcast
Note that broadcast works only on one network (i.e. a single LAN). You can’t scale this approach to internet-wide (why?)
  Limited by bandwidth and computation
To use, simply set the destination address of Datagram Packets to the broadcast address
  Because receiving is forced, you have to listen… up at the operating system level, where traffic consumes cycles and power

## Slide 6: Multicast
Multicast is a much more sophisticated version of broadcast. While broadcast is limited to one network, multicast can, if supported by routers, span multiple networks
A multicast address is a special sort of IP in a particular range, 224.0.0.0-240.255.255.255
While normal IP numbers are associated with a specific single host, a multicast address is best thought of as a group alias that multiple systems can subscribe to.
Each address can have a full range of UDP ports

## Slide 7: Multicast
A host subscribes to a multicast address
Another host sends a UDP packet to a multicast address
Every host that is subscribed to that multicast address receives that packet
Works just like broadcast on a single network
On multiple networks, the packet is sent to other networks only if there is a host on that network that is subscribed

## Slide 8: Multicast
Multicast is a special type of UDP
Use MulticastSocket, a Java subclass of DatagramSocket
MulticastSocket socket = new MulticastSocket(4545);// port
socket.joinGroup(addressOfMulticastGroup); // reserved IP
packet = new DatagramPacket(buffer, buffer.length,
addressOfMulticastGroup, port);
Socket.send(packet);

## Slide 9: Broadcast vs Multicast
For shared network packets, which to choose?
Never pick broadcast!
Always pick multicast (if you are allowed)… It does everything broadcast can do, and also can optionally span networks if router support is present.
OTOOH for backwards compatibility and legacy reasons you might sometime need to use broadcast. So be aware.
Notes: OTOOH = on the other other hand…

## Slide 10: Multicast
On a single network you don’t need any configuration to allow use of multicast
  (except NPS in August 2024…)
On a single network if you have fancy switches you can use something called “IGMP snooping” to reduce extraneous traffic. (Intentional listening/ignoring)
Limited commercial deployment to home; deployments, if any, are mostly within a single enterprise. YMMV!
Notes: YMMV = Your Mileage May Vary

## Slide 11: Client/Server Designs
Q: How should participants talk to each other?
A: It depends. (Again.)
  Peer-to-Peer: shared among many, each host communicates directly with the other hosts.
  Client/Server: Each client talks to a server, and the server distributes information to peers. Peers do not directly talk to each other.
  Various hybrid solutions are also possible.

## Slide 12: P2P, client/server
It’s perhaps a bit easier to think about peer-to-peer (P2P) in the military world
  Often simulations run in one lab, hard to scale.
  Home and enterprise may well be locked down.
For assorted security reasons, client/server (C/S) is most popular today in commercial apps; widespread use of P2P in DoD apps.
State of the art commercial: C/S, UDP, then TCP for content distribution and registration.

## Slide 13: P2P
Most commercial customers are behind a NAT, and it is difficult to establish connections from outside to a host inside a NAT
  Network Address Translation (NAT)
Firewalls prevent connections on unapproved ports.
You simply can’t trust content from general public. In gaming, griefers try to subvert other players (and also the vendor).
In Defense applications you can get away with P2P because of higher trust level, and (theoretically) secure end-to-end control of network configuration.

## Slide 14: anycast
anycast delivers a message to any one out of a group of nodes, typically the one nearest to the source using a one-to-one-of-many association where datagrams are routed to any single member of a group of potential receivers that are all identified by the same destination address.
The routing algorithm selects the single receiver from the group based on which is the nearest according to some distance or cost measure. (Candidate thesis topic here.)
See Content Delivery Network (CDN)