## Slide 1
Distributed Interactive Simulation 101:
The Basics
Don McGregor, Naval Postgraduate School
Don Brutzman, Naval Postgraduate School

## Slide 2: Learning Objectives
What standards are used in distributed simulations in the military?
What types of networking protocols are used?
What needs to be standardized, and what can be different among simulations?
How can we use dead reckoning (DR) to reduce network traffic?
What coordinate systems are used?

## Slide 3: Topics
What is distributed simulation?
Military modeling & simulation distributed simulation standards
Underlying TCP/IP networks
DIS: Entity State PDUs
DIS: Entity Types and Entity IDs
DIS: Coordinate Systems
DIS: Shooting
DIS: Research Topics
Bibliography

## Slide 4: Distributed Simulation Terms
A distributed simulation runs on multiple cooperating hosts on the network
State information describes the position, orientation, and other information about an entity at a point in time
Live, Virtual, Constructive (LVC) simulation involves different hosts doing different aspects of simulation in one cooperative system
  Live: Real people, real systems
  Virtual: Real people, simulated systems (human in loop)
  Constructive: simulated people, simulated systems (AI controlled)

## Slide 5: Live, Virtual, Constructive Example
Automatic Identification System (AIS) is a standard for transmitting the current position of commercial ships in the real world; ships have a transmitter and receiver on board and send information in a standard format. This is a live component (real system, real people)
Ship simulators portray a simulated virtual view of navigation from the perspective of a ship’s bridge, perhaps in a “cave” environment with wall-sized screens. This is a virtual component (real people, simulated system)
We can also inject simulated, computer-generated ships controlled by AI into the simulation. This is a constructive component (simulated system controlled by simulated people)

## Slide 6: Live, Virtual, Constructive Example
Virtual:
bridge simulator
Live: AIS
Single
Shared LVC
Environment
Constructive: computer-
generated ships controlled
by AI

## Slide 7: What Do We Want to Do?
People who want to learn about Distributed Interactive Simulation (DIS) usually are in the “virtual” or “constructive” domains, though it can also be used in the live domain
They want to simulate ships, tanks or other entities in the 3D world, controlled by humans or AI
We need to exchange state information between hosts on the network about entities in the world
  To view someone else in the simulation, we need to know their position, orientation, and other state information, and this information needs to be sent to us by them
Typically entities are controlled by different hosts that are connected via a network. The state information is usually exchanged over the TCP/IP protocol

## Slide 8: State Information in Distributed Simulations
State Information
Location, Orientation, Velocity, etc of Entities
Sent over a TCP/IP network
Tank Simulator
Helicopter Simulator
Notes: The tank & helicopter in the simulation are controlled by different hosts. The simulation running the tank needs to know about the helicopter’s position, and the helicopter needs to know about the tank’s position
We have to come to all sorts of agreements to exchange information. It’s harder than it looks!
We want the information to be in a standard format, because we don’t want to be locked into one vendor

## Slide 9: What’s So Hard?
The format of state update messages needs to be exactly specified.
  What coordinate system should you use? You need one that works well for ground and air systems, and can handle curvature of the earth issues.
  Text or binary format messages?
  The order in which the fields appear?
Network issues: what happens if a message is dropped?
Scalability issues: how can we get a reasonable number of entities to participate?
Latency: can we keep the message delay reasonable?

## Slide 10: Distributed Simulation Standards
There are many ways to exchange the state information, but we want a standard way so we can interoperate with simulations from many vendors rather than being locked in to one. We don’t want to use only one vendor’s proprietary method, for which we will pay dearly
In the case of defense modeling and simulation, the big three are
  TENA: Test and Training Enabling Architecture
  HLA: High Level Architecture
  DIS: Distributed Interactive Simulation
TENA and HLA borrow many semantic concepts from DIS. Understanding DIS has many carry-overs to other standards

## Slide 11: State Information Exchange Standards
Controlling Host
Receiving Host
DIS
HLA
TENA
The controlling host sends the state information update
via one of the standards to other hosts
State Information Updates

## Slide 12: TENA
Used on ranges; often the “L” in Live-Virtual-Constructive simulations
Designed for real time and embedded systems, real sensor systems, etc.
In effect it is thinly disguised CORBA distributed objects with some new features to help it work in a simulation environment
Can gateway it to other standards, such as DIS or HLA
See http://tena-sda.org

## Slide 13: High Level Architecture (HLA)
HLA is very general and intended to cover most of the defense modeling domains including training, analysis, and engineering in addition to virtual worlds
Participants communicate via an agreed-upon Federation Object Model (FOM) and an API associated with a Run-Time Infrastructure (RTI)
Specification is maintained by SISO (http://sisostds.org), is IEEE standard 1516 and has implementations by MAK (http://www.mak.com), Pitch (http://www.pitch.se), Portico (older version) (http://porticoproject.org) plus Mak (http://mak.com) and others
http://www.pitch.se/hlatutorial is a good introduction to HLA
Notes: HLA

## Slide 14: Distributed Interactive Simulation (DIS)
DIS was the first standard to tackle these problems in a systematic way
Originated in the SIMNET project in the 80’s. DARPA supported converting the SIMNET research into a standard; SISO developed the standard and took it to IEEE for approval.
This means anyone can get the standard from IEEE, implement it, and participate in a simulation
Development of standard continues; updated DIS standard version 7 is the latest approved version. SISO maintains the standard and presents it to IEEE for standards approval
Substantial commercial support, open source implementations, many home grown implementations of portions of the standard

## Slide 15: Distributed Interactive Simulation (DIS) functionality
What is it?
  A standardized way to exchange messages about entities in a virtual world
  Common semantics for coordinate systems and other information, such as how to describe and specify entities
  Common practices to ensure interoperability

## Slide 16: Networking: the Protocol Stack
DIS defines the format of the messages, but doesn’t specify how to get the messages from one host to another. Almost always this is done via TCP/IP
Link and Physical
IP
TCP Sockets
Application
DIS Implementations
How messages are
transmitted between
hosts: TCP/IP
protocol, implemented
by host operating
system
UDP Sockets
Notes: TCP/IP is the underlying substrate for almost all network communications. Web servers, streaming video, email and almost everything else you use on the internet all rely on TCP/IP
Users typically implement things at the “application layer” at the top of the stack. This is where DIS lives
  Somewhat confusingly, the DIS protocol is considered part of the “application layer” in addition to what users think of as the “application”, the visual simulation
The lower layers of the stack are responsible for delivering messages. We can usually ignore this part; it’s all handled by operating system vendors
We interact with the TCP/IP stack via either the User Datagram Protocol (UDP) or Transmission Control Protocol (TCP) APIs.
UDP messages are like postcards: they contain a fairly small amount of data, and we need to address them to a destination
  We can send them to one host (based on IP number): called unicast
  We can send them to all hosts on a local network: called broadcast
  We can send them to those hosts, on the local network or not, that are interested in the message: called multicast
DIS messages are contained inside of UDP packets and can use any one of these addressing schemes. Broadcast is very common. Multicast is better.

## Slide 17: TCP/IP and UDP
TCP sockets have higher latency, higher jitter (variation in latency), and doesn’t scale to large numbers of hosts as well
UDP sockets have lower latency, lower jitter, scales to large numbers of participants better, but are unreliable
DIS typically uses UDP
Hold on—UDP is unreliable? What’s up with that?
  Individual UDP messages may be dropped by the network; there’s no guarantee that a UDP message will be delivered. This is a tradeoff to achieve lower latency and jitter, and better scalability
  This is not as big a deal as it might seem. If we’re getting position updates from an entity every 1/30th of a second, does it matter if we drop one? We have better information coming along shortly, so why try to resend the dropped message?

## Slide 18: DIS Messages
We know what we want to do: send a message that tells another host what the state of an entity is
We know how we do this: we send the message via TCP/IP, typically in a UDP message over broadcast or multicast
What is the actual format of the messages? This is specified by the DIS standard.
  There are dozens of possible messages to send, relating to everything from logistics to electronic warfare to radio communications
  Each message type is called a “Protocol Data Unit” (PDU)

## Slide 19: DIS Messages
PDU
Entity Information
Entity State
Collision
Warfare
Fire
Detonate
…
Several dozen different messages (called Protocol Data
Units, or PDUs) to describe entity movement, collisions,
combat, radio communications, logistics, and more. The
Entity State PDU is the most widely used
19

## Slide 20: DIS Messages: Entity State PDU
We use ESPDU when want to inform other hosts of the position of an entity we control—the most common PDU
Entity sends ESPDU with
• Unique ID
• Position (xyz) in standard coordinate system
• Orientation
• What type of vehicle it is
• More….

## Slide 21: Entity ID: a Unique Identifier
Before we can tell an entity “hey you, do that” we need a way to differentiate between entities
The entity ID is a unique identifier for each simulation object in the world. In DIS this is done via a triplet of three numbers: the Site, Application, and Entity
These three numbers taken together must be unique for each entity

## Slide 22: DIS: Entity IDs
Example: before the simulation starts we agree, simulation-wide, on the following arbitrary numbers. Here are simple possibilities:
Site | Number
China Lake | 42
Norfolk | 17
Orlando | 23
Application | Number
YoYoDyne M1A2 Simulator | 112
ACME UCAV Simulator | 417
JCATS | 512

## Slide 23: Entity IDs
Tank Simulator
EID: (42, 112, 18)
EID: (42, 112, 19)
Helicopter
EID: (17, 417, 18)
ACME (417) simulator at
Norfolk (17) controls a
Helicopter (entity 18)
YoYoDyne simulator (112) at
China Lake (42) controls two
distinct tanks, 18 and 19

## Slide 24: DIS: Entity Type
We may need some other information. What if we want to draw this entity? We need to know what this is—a tank, a helicopter, a ship?
This is done via something called the Entity Type, which in turn depends on a SISO document called the “Enumeration and Bit Encoded Values” (EBV).
The EBV document is a long listing of standardized record values that lets us identify military hardware

## Slide 25: Entity Type
{
Kind: 1 (entity)
Domain: 1 (Land)
Country: 225 (US)
Category: 1 (Tank)
Subcategory:1 (M1)
Specific: 6 (M1A2)
}
Whenever a DIS message has an entity type record with the above settings
we know it’s referring to an M1A2 tank. What the numbers are doesn’t
matter, as long as all participants agree on what they mean. SISO maintains
this list of arbitrary numbers, called the EBV document

## Slide 26: Entity Type From EBV Document

## Slide 27: Entity Type
The EBV document has gone through many versions as new hardware has been added. An important checkpoint for consistency: all participants in the simulation should agree on the version of the EBV document used.
In reality this is hard; some simulations have not been updated to reflect new EBV documents, and sometimes those implementing a simulation simply make up numbers, and no simulation implements all entities in the EBV.
You may need a gateway such as Joint Simulation Bus (JBUS) to act as a “shim” connection between simulations and change entity type values to match what is expected. The gateway can rewrite the entity type values in the PDUs to force them to match expectations.
The EBV enumerations are also often used in HLA RPR-FOM and in TENA.

## Slide 28: Entity State PDU: Position
What does it mean if we say an entity is at (x, y, z)? This has no meaning without a coordinate system. We need to agree on one, and where the origin is
DIS chose to use a Cartesian, geocentric coordinate system because
It’s easy to convert from that to other coordinate systems, such as geodetic
(latitude, longitude, altitude) or military
Systems such as MGRS
Notes: If you want to specify the location of an entity in DIS, you have to specify it in terms of how far from the center of the earth it is. You should also agree on the shape of the earth (eg WGS-84) and terrain
Using geocentric coordinates may seem strange, but DIS has to account for curvature of the earth issues if the simulation demands it. The geospatial people have done the math to convert geocentric coordinates to latitude, longitude, altitude, MGRS, or other coordinate systems. The geocentric coordinate system is often used in TENA and HLA
SEDRIS has provided an open source framework for dealing with these issues in their Spatial Reference Model (http://www.sedris.org/hdr1trpl.htm)

## Slide 29: DIS: Coordinate Systems
Very often simulations set up a local, flat-plane coordinate system at a point tangent to a point on the earth’s surface, and use that for local physics and movement. When the ESPDU is actually sent the local coordinates are changed back to the global coordinate system. The SEDRIS SRM package can do the math
Nobody will ever agree on which way the local coordinate system axes should point for all simulations

## Slide 30: Coordinate Systems
X
A local Cartesian coordinate system origin is set at {lat, lon, alt}. The simulation
does all its calculations and movement in this coordinate system, because it’s convenient. Before
sending entity information out in a DIS ESPDU, convert from local to geocentric
(DIS) coordinates
Local coordinate system origin
At lat 43.21, lon 78.12, alt 120m, WGS 84
X (East)
y (North)
Entity position can be expressed in:
Local: (10, 10, 4)
Geodetic: 43.21001 N, 78.12012W, 124
UTM: Zone 44N, 266061E, 4788172N, 124M
DIS: 958506.1, 455637.2, 4344627.4
We have enough information to convert
from one coordinate system to another if we know the local coordinate system origin!

## Slide 31: DIS: Dead Reckoning (DR) Algorithms
If we’re running a visual simulation, how often do we need to send ESPDUs?
If running at frame rate, maybe about every 1/30th of a second.
  If we have 500 entities in a simulation, this can work out to 15,000 UDP messages per second. If you’re doing other computation on the host this will tax your CPU and network
Do we really need to send that fast? If we know how fast and in what direction an entity is moving, we can dead reckon in between receiving an ESPDU and draw our entity there.
  Sure, we’re lying to the user. Got a problem with that? If our DR is wrong, we just correct our position stealthily when we get better info on the next packet. The user won’t know the difference, probably.
  Due to latency all simulation participants are a little out of sync anyway

## Slide 32: DIS: Dead Reckoning
Time
ESPDU Updates
Aircraft position & orientation updated by dead reckoning updates between ESPDU messages
ESPDU 2
ESPDU 3
DR updates

## Slide 33: DIS: Dead Reckoning
What DR algorithm is best? (… wait for it…)
It depends! In some situations we might want to include acceleration or angular velocity, but not in others. The ESPDU sender specifies what DR algorithm to use
The sender can also perform its own DR to determine what the recipients are seeing. If the sender decides the clients are probably wrong in their guess about where the entity is, it can issue another ESPDU with better location information

## Slide 34: DIS: Learning About the World and Heartbeat
If we’re running a DIS simulation, how do we learn about all the other entities in the world?
  One design choice DIS could have chosen is to use a server. Instead, the designers chose for DIS to be peer-to-peer; there is no central server, and hosts talk to one another directly
In DIS all we have to do is listen for ESPDUs. The ESPDUs contain what we need to know: entity type, location, velocity, orientation. This is simple and avoids a single point of failure, and makes configuration easy
  There are also Simulation Management PDUs for announcing arrival, removal, etc.
To make this work, every entity must periodically send a time-stamped ESPDU even if its state hasn’t changed. This is called a heartbeat. Usually entities must send an ESPDU at least once every five seconds

## Slide 35: DIS: Timestamp
One of the oddities of UDP is that UDP packets may be duplicated during TCP/IP routing; we send a single packet, but two might arrive nevertheless.
UDP packets may also arrive out of order. We send packets in order A, B, C, but they arrive in order C, A, B
  This creates problems for position updates! How to handle? ....
DIS includes a timestamp field to detect these kinds of problems
  The field typically represents time since the top of the hour (as common practice)
  If the next packet we receive has a timestamp before the last packet we processed, we can discard it; it’s old information that has been obviated by new data
  Time coordination between hosts useful but not required

## Slide 36: DIS: Timestamp
Host A sends 1 and then 2. Host B receives 2, and then 1.
We should discard 1, because we know it’s older than 2,
due to its older timestamp.
2
1
1
2

## Slide 37: DIS: Entity State PDU
So far we’ve looked at an ESPDU, which contains
  Entity ID
  Entity Type
  Position, orientation, velocity, etc
  Specifies a DR algorithm for the receiver to use
  Timestamp
We’ve also seen that we need to agree upon a coordinate system, and agree on the enumerations that describe things like entity type.

## Slide 38: DIS: no approved Application Programming Interface (API) per se
DIS doesn’t have an API. This seems strange to people coming from HLA or TENA, but reflects common practice in networking protocols
  The standardized part is the format of the messages on the wire. The standard is silent about how to create or receive those messages
  Different DIS vendors have different APIs, but all produce the same format messages. This is in contrast to HLA, which has a standard API, but is silent about the format of messages on the wire. As a result, different HLA RTI vendors usually use different message formats for exchanging information
  TENA standardizes the API, and there is a single approved implementation of the RTI equivalent; this sidesteps the wire standard problem because there is only one approved equivalent of the RTI

## Slide 39: DIS: Message Format Standardized
Vendor A API for DIS
Vendor B API for DIS
Vendor C API for DIS
Standard Format Messages
JCATS Sim Code
ACME Sim Code
ONE-SAF Sim Code
Network

## Slide 40: HLA: API Standardized
HLA RTI API
HLA RTI API
HLA RTI API
RTI Vendor-Specific Format Messages
JCATS
ACME Sim
ONE-SAF
Network
While the API is standard, implementations of the HLA RTI API from different vendors are allowed to produce messages in different formats.

## Slide 41: DIS: API
The implications of this are that while HLA has a standardized API, RTIs from different vendors can’t typically talk directly to each other. This makes changing vendors easy, but makes getting RTIs from different vendors talking to each other hard--you need to use a gateway
DIS in contrast makes changing vendors hard (since it involves changing the API your simulation code uses) but talking between vendors easy (since all the messages on the wire are in the same format)
  The lack of an API can help when using unusual languages, such as Objective-C, C#, Python, and Javascript. Since there’s no API, just make one up. As long as they produce standard messages, it doesn’t affect anyone else

## Slide 42: DIS: PDU Format
Remember, all this information is being sent in binary format in (typically) a UDP packet
The exact format that an ESPDU must have on the wire is specified in the DIS standard. This includes byte order
For example, the EntityID field starts 12 bytes into the ESPDU message, is in the order (site, application, entity), and each field entry is 16 bits long, in network byte order, and unsigned

## Slide 43: DIS: ESPDU Format

## Slide 44: DIS: Looking at ESPDUs
What do ESPDUs look like? We can examine them on the network with a free tool called Wireshark, which can decode DIS packets
  http://www.wireshark.org
Remember, it’s the format of the messages on the wire that count. The DIS standard specifies the exact format of binary messages, and any tool that produces or consumes those messages is fine with DIS. How you create them is none of DIS’s business

## Slide 45: Wireshark: Capture Packets

## Slide 46: Wireshark: Decode Packets as DIS

## Slide 47: Wireshark: Examine DIS Packets

## Slide 48: DIS: Implementations
Format
  We know what information we want to send: entity type, entity ID, position, orientation, etc.
  We know what coordinate system we want to use
  We know where to find arbitrary, agreed-upon enumeration identifier values—the EBV document
  We know some PDU types: entity state PDU, etc.
How do we get the information into the format we want on the wire?
This is where DIS implementations come in

## Slide 49: DIS: Implementations
Where can you get a DIS implementation?
  Write your own (cough cough)
  Buy one. There are several commercial implementations and many have excellent support
  Use an open source version—”free as in free puppy”
    Open-DIS (https://github.com/open-dis - formerly http://open-dis.sourceforge.net)
      Java, C++, C#, Objective-C, JavaScript, Python
    KDIS (http://sourceforge.net/projects/kdis)
      C++
    Aquarius (http://sourceforge.net/projects/aquariusdispdu)
      C++
    JDIS (http://sourceforge.net/projects/jdis)
      Java

## Slide 50: DIS: Sending
Remember, DIS has no official API. Every implementation is different. This example will use the Open-DIS API codebase. Implementation available at https://github.com/open-dis
Source code for this example is available at http://www.movesinstitute.org/DIS
The example contains a lot of supporting libraries for other things. Ignore all that for now.
All code is BSD open source license; nonviral, use any way you see fit

## Slide 51: DIS: Send ESPDUs in Java

## Slide 52: DIS: Send PDUs in Javascript
Can use HTML5 Browser geolocation and Javascript to send
DIS from a web page

## Slide 53: DIS: Receive PDUs in Java

## Slide 54: DIS Sending and Receiving PDUs
There are similar idioms for other languages such as C++, Objective-C (IOS/MacOS), Javascript, Python, C# (Windows phone, Unity 3D)
Note that this requires that you do a bit of socket programming, which TENA and HLA hide from you. Socket programming isn’t that bad…

## Slide 55: Visualizing DIS Data via Online Map using DISWebGateway
DISWebGateway running at
http://track.movesinstitute.org
  Java sender & receiver for DIS
  Can receive native DIS from existing DIS applications
  Web-based map that shows DIS entity locations

## Slide 59: DIS: Shoot at something
We’ve been sending ESPDU messages back and forth, but there are dozens of other sorts of messages. What if we want to shoot at someone? What does this involve?
We can use a Fire PDU, which contains
  The entity ID of the shooter
  The entity ID of the target (if known)
  The type of munition being fired, fuse, quantity, etc. This is very similar to the entity type
  Enough information to compute the path of the munition (if desired)

## Slide 60: DIS: Shoot at Something
The Detonation PDU usually follows a Fire PDU. It contains
  Location of detonation, shooter entity ID, target entity ID
  Fuse, munition type, and so on
When a Detonation PDU is received simulations assess the damage to their own entities. This means simulations are on the honor system for determining damage; James T. Kirk can Kobayashi Maru

## Slide 61: DIS Shooting
Fire! I’m entity (17, 23, 42), shooting
at entity (123, 7, 12) with a HEAT round
from (x, y, z)
Explosion! There’s an detonation of a HEAT
round at (x’, y’, z’).
All entities now assess the damage to themselves by the
Detonation at (x’, y’, z’)

## Slide 62: DIS: Arbitrary Data
You can also exchange arbitrary data between DIS simulation participants with the DataQuery and Data PDUs.
  Participant sends a DataQuery PDU addressed to another participant
  That participant responds with a Data PDU
The data itself is sent as “fixed variable datums” or “variable data datums”. Therefore it’s up to you to specify the exact format of these

## Slide 63: DIS: Other messages
There are many other messages that can be used in DIS
  Electronic warfare
  Logistics
  Directed energy weapons
  Voice/Intercom
  Collisions
  Simulation management
  Data exchange
It’s a big topic!
But the basics are: a standard format for exchanging state information

## Slide 64: DIS and Other Standards
How can DIS interoperate with HLA or TENA?
HLA Real Time Platform Reference Federation Object Model (RPR-FOM) is closely modeled on DIS
  Same entity types, same entity IDs, same coordinate system, very closely matches DIS
  This was done to make transition from DIS to HLA easy
  There are several gateways to translate between DIS and RPR-FOM. JBUS is one, several commercial
TENA has a generalized gateway functionality that can map TENA events to DIS and vice versa. It generally uses the same coordinate system, entity types, etc.

## Slide 65: DIS Research Topic: DIS in the Web Page
Websockets are a standard from IETF and W3C. The idea is to provide a direct Javascript-based TCP socket into a web page without having to use AJAX polling techniques. Widespread browser support
Javascript is a widely used language for dynamic web content
  WebGL is Javascript binding for OpenGL which allows us to use accelerated 3D graphics inside the web page
  WebGL can be the substrate for higher level graphics standards such as X3D
Put all three together and you can implement a networked virtual environment in a web page

## Slide 66: DIS Research Topic: 3D in the Web Page
Web Server
Network with
conventional
binary DIS
Web pages with Javascript
WebGL scene updated by
DIS over a Websocket

## Slide 67: DIS Research Topic: 3D in the Web Page

## Slide 68: WebLVC
The combination of this—WebGL, WebSockets, and fast Javascript in the web browser—has emerged recently
Can send DIS directly into the web browser
SISO WebLVC Working Group
  http://discussions.sisostds.org/topiclistview.aspx?fid=256
See also Virtual World Framework
  http://virtualworldframework.com
Active research topic

## Slide 69: Summary
DIS works by exchanging state information over the network.
Not an API standard, but different APIs can implement.
Focused in virtual and constructive simulations.
A series of binary format messages, with the format exactly defined.
Entity types, entity IDs, heartbeats, and coordinate systems.

## Slide 70: Bibliography
SISO: http://sisostds.org
SISO DIS Protocol Support Group: http://discussions.sisostds.org/topiclistview.aspx?fid=32
Open-DIS: http://open-dis.sourceforge.net
SEDRIS SRM: http://sedris.org
Kdis: http://kdis.sourceforge.net
Wireshark: http://wireshark.org
WebGL: http://www.khronos.org/webgl
X3D: http://www.web3d.org http://x3dgraphics.com/slidesets
WebLVC: http://discussions.sisostds.org/topiclistview.aspx?fid=256
WebSockets: http://tools.ietf.org/html/rfc6455 , http://www.w3.org/TR/websockets